## Slide 1: PID Design for eLOI
RIKEN/RBRC
Itaru Nakagawa

## Slide 2: Table of Contents
Requirements
  Kinetic Coverage (p, rapidity)
Technological Choice, Existing Detectors
ePHENIX Design Concerns
  RICH (Forward)
  DIRC (Central)
Photon Detector

## Slide 3: Required Kinetic Coverage and Spatial Constraint
Forward Arm
  B-field
  Path length < 1m
  Shoot for 4 < pi/K/p < 50 GeV
Central Arm
  B-field
  Path length 10 ~ 30 cm
  Shoot for pi/K/p < 5GeV
5x100
10x250
p
h

## Slide 4
RICH
GEM
Station4
EMCal
HCal
GEM
Station2
z (cm)
R (cm)
HCal
p/A
EMCal
GEMs
EMCal & Preshower
μ-TPC
DIRC
η~1
η~4
-1.2
R (cm)
GEM
Station3
GEMs
Station1
η~-1
e-
AreoGel

## Slide 5: PID @ LHCb

## Slide 6
RICH-1 (modern HERMES RICH) RICH-2
2<p<60 GeV 17<p<100 GeV
25-300 mrad 10-120 mrad
5cm Aerogel (n=1.030) ~200 cm CF4 (n=1.0005)
85 cm C4F10 (n=1.0014)

## Slide 7: LHC-b HPD based Photondetector
3 m2 area have been equipped with photodetectors providing:
Single Photon Sensitivity (200 - 600nm)
2.5 x 2.5 mm2 granularity
Fast readout (40 MHz)
Active-area fraction > 70%
Hybrid Photo Diodes (HPD)
340 k channels

## Slide 8: LHCb RHIC Performance
Achieved excellent PID for wide momentum range.

## Slide 9: RICH Performance Simulation
Apply Momentum Measurement Resolution
PYTHIA Momentum Distribution
Choose Momentum Range
Compute Cherenkov Angle for Chosen Momentum Range
,
n = 1.00062
Apply Cherenkov Angle Measurement Resolution
= 0.05*
Compute Mass for Different Particles
m =
Study by Tuya Erdenejargal @ Colorado

## Slide 10: Expected Purity (for Ideal Case)
Study by Tuya Erdenejargal @ Colorado
dp/p = 0.5%, dq/q=1% assumed

## Slide 11: ePHENIX Strategy
CsI-GEM (RICH)
RICH
AreoGel
1m
Path length
B-Field

## Slide 12: Technological Challenge for eRHIC
Photon Detector
  (Hybrid) PMT doesn’t work in B-field
  -> ePHENIX Choice : R&D fund for CsI-GEM

## Slide 13: R&D Objectives
Test of Ring-Imaging Cherenkov detector prototype
  Photocathode in field
    CsI-GEM
  Mirror in deep UV
    MgF2 coating
  Single Photon Capability
    quintuple GEM stack with APV25-SRS
  Radiator choice:
    CF4

## Slide 14: Test Beam May/June @ SLAC
Spherical mirror makes ring:
  Ring  Cherenkov Angle
Here: system running w/ 55Fe.
Readout APV25 via SRS.
Ready for Test Beam.

## Slide 15: First Results: Rings and more
Home-grown DAQ allows us to readout SRS and FADC to get chamber and beam counters into single data file.
RINGS!!!!!!!!!!
Data taken:
  FWD & reverse bias.
  Gain Scans
  Relative GEM variation

## Slide 16: Central PID
Central PID:
Mid rapidity has some high momentum tracks, but most are in hadron direction.
PID detector works in tight spatial constraint 10 ~ 30 cm, technology choice is DIRC. DIRC distinguish p-K up to ~4 GeV.
For SIDIS, cut on z= P•p/P•q
z>0.2 standard cut
Can measure dark blue
region in central arm
5x100
10x250
p
h
h>1
Q2
x
Max z in |h|<1

## Slide 17: BaBar Detector

## Slide 18: DIRC
DIRC (Detection of Internally Reflected Cherenkov light)
Path length ~ 10cm
Quartz as radiator and as light guide
Effective at low momenta
(p < 4 GeV/c)
The only existing DIRC was in
operation at BABAR
PANDA is planning two

## Slide 19: Principle of DIRC
Slide from Thomas Hdig, 3rd Workshop on Higher Luminosity B Factory 2012

## Slide 20: Reflaction Index
<n1> = 1.473
n3 (nitrogen) ~ 1

## Slide 21: RING Image of DIRC
Slide from Thomas Hdig, 3rd Workshop on Higher Luminosity B Factory 2012

## Slide 22: DIRC Performance
Plot from Jochen Schwiening, RHIC2004
SLAC-PUB-10516

## Slide 23: Efficiency and Mis-ID

## Slide 24: Summary and Ideas
Study in progress to achieve as close as possible to the established performance of other facility COMPASS/LHCb within ePHENIX constraint (B-field, spatial constraint.
Focusing DIRC (intended design for Super-B). Compact enough to employ SiPM for better qc measurement + fine timing measurement.
Microchannel Plates Detectors instead of Aerogel.
TPC+HBD hybrid to expand PID in higher momentum region. (P20 of Jin’s Talk)

## Slide 25: Backup

## Slide 26: TPC/HBD Design Progress
Central arm tracking via TPC.
Central arm dominantly low p.
  Low Mass Tracking.
  Hadron ID from dE/dx.
  eID from Cherenkov “blob”s.
  Prototype design progressing.

## Slide 27: SINGLE PHOTON DETECTORS
the requests:
QE: high QE (above standard PMT photocathodes having peak-values of 20-25 %)
r: rate capabilities (> 100 kHz/ mm2)
t: time resolution below 100 ps
B: insensitivity to high magnetic fields (B=1T and more)
$: reasonable costs to make large systems affordable
L: Large area and wide angular acceptance of each single sensor
the approaches:
Poly- and nano-crystalline diamond-based photocathodes (QE)
Photocathodes based on C nanotubes (QE)
Hybrid avalanche photodiodes HAPD (B)
Si photomultipliers (QE,r,t,B)
Microchannel plate (MCP) PMTs (B,t)
Micro Pattern Gas Detectors (MPGD) + CsI (r, B, $)
Large, wide aperture (hybride) PMTs (L)
astroparticle experiments
promising
for a far
future

## Slide 28: Magnetic Field Effect
dispersion < 5% of θMAX
The RICH sits in a magnetic field and causes some ring irresolution
A lot for the lower eta tracks (irresolution is 30% of size of max ring).. Still working to reduce (some amount will be correctable through reconstruction)
At high eta it is small compared to irresolution due to momentum measurements

## Slide 29: Focusing
R (cm)
Z (cm)
RICH Mirror
Entrance
Window
RICH Gas
Volume
Mirror Center:
Z = 100 cm
R = 40 cm
Focal plane and photon detector
η=1
η=2
η=3
η=4
IP center
GEM
Station2

## Slide 30: Purity
Study by Tuya Erdenejargal @ Colorado
dp/p = 0.5%, dq/q=5% assumed

## Slide 31: Some fast results already
Sasha reexamining his work for MIE:
  Do we need measure below 2 GeV?
    Would require much better hadron rejection
    Can we use event topology to get better rejection

## Slide 32: Results from task force
Central EMCal energy resolution (5x100):
For MIE studies, looked at 5x100 and 20x250 to see extremes. For LOI, use 5x50 and 10x250.
h<-1
|h|<1
h<-1
|h|<1
In MIE, assumed Q2<1 is uninteresting, but will revisit.
Also argued that hadron rejection fine if Ee>2, and below 2 GeV, little phase space, so no loss.
Sasha revisiting these assumptions after feedback from EIC group.

## Slide 33: COMPASS

## Slide 34: COMPASS PID
PLB673 (2009)127
NIM577 (2007)455 ->

## Slide 35: 5x50: Minimal energy cut
Ee<1GeV
Ee<2GeV
Not so much of Q2&x space is lost but it corresponds to quite some range in y (important for FL, DVCS etc).
How crucial is the lost of y>0.6 or y>0.8?
Similar effect at 10x250
Preshower to get better hadron rejection?
Ee<2GeV
Ee<1GeV

## Slide 36: Results from task force
Momentum resolution requirements:
Requirements for momentum in forward direction not so stringent
Angular resolution requirement at small angle will more important
5x100
5x100
5x250
5x250
dp/p
dq