## Slide 1: Activity of high-rate detector consortium & status of detector developments
Masaki Sasano
RNC
On behalf of the consortium

## Slide 2
Idea
Technology
Implementation
& operation
Scientific knowledge
What should be discussed…
Scientific societal benefit
RIBF
users
Local researchers at RIBF
BigRIPS team
Consortium
Detector team
Need to minimize
Human resource, budget, time for
setup
operation
maintenance
Death valley:
Matching needs
Marketing research
Building management (operational)
framework
….

## Slide 3: Goal (Matching needs)
To achieve:
a total intensity  ~ 3 - 5 x 100k Hz (after F7)
(at present, BigRIPS can accept 30 – 50 kHz, Z>=50)
Clear PID for nuclei for Z=50 or heavier
Standard setup

## Slide 4: How to define “high rate”?
Rate available for users on reaction target
~ 3 - 5 x 100k Hz (after F7) or higher
  In the upstream, the beam rate can be higher:
  F3 > F5 > F7 (“>” can be a factor of 10—100 or higher, depending on RI)
  In focusing points, F3 and F7, the beam spot size is small, so the rate capability must be considered taking into account how the detector is segmented.
  Undetected light particles also matter:
  Tritons (when one studies neutron rich side around or over A/Z=3)
  F3 > F5 > F7
  How many days can work continuously?“
  For example, in the recently done 132Sn experiment at ZDS with 40-50kpps in total after F7;
    F3 PPAC  1 day
    F8/9/11  2 days
     replacement

## Slide 5: Member list (2014/1/19)
Daiki Nishimura, Tokyo University of Science
 IC
Hidetada Baba, RNC, →DAQ, Flash ADC, FPGA
Meiko Kurokawa, RNC →ASIC, Si detectors, …
Toshio Kobayashi, Tohoku Univ.
→MWDC, 1-mm MWPC, CRDC,
Hideaki Otsu, RNC →MWDC, MWPC, IC,
Yohei Matsuda, Kohnan Univ.→detectors
Shinsuke Ota, CNS, Univ. of Tokyo  MWDCs, …
Juzo Zenihiro, RNC →indirect method for charge determination
Kimiko Sekiguchi, Tohoku Univ.
P. Rykaczewski (ORNL) →Flash ADC based DAQ
Stephanos Paschalis (Darmstadt)
Zoltan Elekes (ATOMKI)
Nigel （LP CAEN）
→ TDC/QDC (within some limit, dead time free)
Emmanuel Pollacco
→ Detectors, Electronics, ASIC chips, GET…
Alexandre Obertelli, CEA Saclay
Tuomas Grahn, University of Jyväskylä
Megumi Niikura, University of Tokyo
Masaki Sasano, RNC  chair, IC
Yohsuke Kondo, TITECH
Nori Aoi, RCNP Osaka University
Nobuaki Imai, CNS, Univ. of Tokyo
Naoki Fukuda, RNC
Kwongbok Lee, Kwon Young Kwan, Moon JunYoung, Institute for Basic Science, Korea

## Slide 6: Materials to be developed
TOF:
Plastic scintillator
Diamond detector
Position:
MWDC
MWPC
CRDC
PPAC
Fiber scinti.
Si strips
Micro Pattern
Charge (Z):
Plastic scintillator
Ion chamber
Silicon detector
Indirect method…
Detectors
Auxiliary systems
DAQ:
Trigger rate
Time stamping
Flash ADC
Electronics:
ASIC chips
Cabling
Vacuum:
Feedthrough
Cooling of ASIC chips
Light tightness

## Slide 7: Other important things to be discussed
Radiation:
Safety
STQ heat load
Hang up of control systems
Running cost:
Detector material replacement
Plastic, gas, …
Manpower:
Development
Maintenance
Operation
Taking over skills…
Initial investment:
Cost for development
Standardization
Test beam time…

## Slide 8: Status of detector development by the consortium members

## Slide 9: TOF detectors
 | Plastic scintillator | Diamond detector
Advantage | Cheap, Easy setup Uniformity??? Can be thin | Radiation hardicity
Disadvantage | Deterioration (especially for higher Z) PMT read out (instability) | Expensive, Fabrication (plating, bonding…) Small size (at present, 30x30 mm) Non-uniformity??? Too thick for high Z?

## Slide 10: TOF detectors
 | Plastic scintillator | Diamond detector
Advantage | Cheap, Easy setup Uniformity??? Can be thin | Radiation hardicity
Disadvantage | Deterioration (especially for higher Z) PMT read out (instability) | Expensive, Fabrication (plating, bonding…) Small size (at present, 30x30 mm) Non-uniformity??? Too thick for high Z?
Yuki Sato-san, Michimasa-san

## Slide 11: Michimasa-san’s work

## Slide 12: Position detectors
 | 1-mm pitch MWPC | MWDC | CRDC | PPAC | TPC
Advantage | > 105 Hz per wire Easy data handling | 105 Hz per wire achievable position resolution Can be large size | Low-z detection Easy cabling Strong for rad. damage | Easy cabling Easy data handling | Only gas material in beam line
Disadvantage (or issues) | Small size (32x32mm2) Skill, manpower Complicated cabling … | Skill, man power Complicated cabling … | Charge readout (weak for noises) | Inefficiency for low-z detection Rad. damage | Long drift time (needs to cover a long range of TDC)
1-mm pitch MWPC@F3 & CRDC @ other focal planes
w/ electronics in vacuum (lower power ASD + FPGA), water cooling?

## Slide 13: Position detectors
 | 1-mm pitch MWPC | MWDC | CRDC | PPAC | TPC
Advantage | > 105 Hz per wire Easy data handling | 105 Hz per wire achievable position resolution Can be large size | Low-z detection Easy cabling Strong for rad. damage | Easy cabling Easy data handling | Only gas material in beam line
Disadvantage (or issues) | Small size (32x32mm2) Skill, manpower Complicated cabling … | Skill, man power Complicated cabling … | Charge readout (weak for noises) | Inefficiency for low-z detection Rad. damage | Long drift time (needs to cover a long range of TDC)
1-mm pitch MWPC@F3 & CRDC @ other focal planes
w/ electronics in vacuum (lower power ASD + FPGA), water cooling?

## Slide 14: Kobayashi-san’s work

## Slide 15: Position detectors
 | 1-mm pitch MWPC | MWDC | CRDC | PPAC | TPC
Advantage | > 105 Hz per wire Easy data handling | 105 Hz per wire achievable position resolution Can be large size | Low-z detection Easy cabling Strong for rad. damage | Easy cabling Easy data handling | Only gas material in beam line
Disadvantage (or issues) | Small size (32x32mm2) Skill, manpower Complicated cabling … | Skill, man power Complicated cabling … | Charge readout (weak for noises) | Inefficiency for low-z detection Rad. damage | Long drift time (needs to cover a long range of TDC)

## Slide 16: Tuomas-san work

## Slide 17: Pollacco-san and Sako-san work

## Slide 18: Z detectors
 | Plastic scintillator | Ion chamber | Silicon strip detectors | Indirect method
Advantage | Relatively easy setup Uniformity | Radiation hardicity Relatively easy operation | Good Z resolution and high rate if highly segmented | No radiation damage No limitation???
Disadvantage (or issues) | Low resolution with small energy loss Radiation damage | Some noise comes from the upstream of F7??? Pileup | Expensive Fabrication Radiation damage | Proof of principle… Combining several detectors

## Slide 19: Daiki Nishimura-san’s work

## Slide 20: Materials to be developed
Auxiliary systems
DAQ:
Trigger rate
Time stamping
Flash ADC
Electronics:
ASIC chips
Cabling
Vacuum:
Feedthrough
Cooling of ASIC chips
Light tightness

## Slide 21: Kurokawa-san and Ota-san’s work on feedthrough

## Slide 22: Summary
In near future, a “high intensity” (total intensity of ~ 3 - 5 x 100k Hz after F7) must be achieved.
Developments are ongoing among the consortium and they can be merged into a standard setup at RIBF.
Need to minimize human resource, budget, time need for setup, operation, and time must be considered.
Some people are already working on very “high intensity” (~> MHz).
Auxiliary system is very important. Feedthrough is a good example.