## Slide 1: RIKEN Workshop on High-Power Heavy-Ion (q/A ≤ 0.5) Cyclotrons
Summary of Workshop
June 26-29, 2015
Hiroki Okuno
Luciano Calabretta
Jong-Won Kim
Jose Alonso
Slides available at: http://indico2.riken.jp/indico/conferenceDisplay.py?ovw=True&confId=1937

## Slide 2: Workshop Participants
Participants | Institutions
Andreas Adelmann | PSI (IsoDAR)
Jose Alonso | MIT (IsoDAR)
Luciano Calabretta | INFN (IsoDAR)
Eric Forton | IBA (Industry)
Sunchan Jeong | IBS (RISP)
Hiroshi Imao | RIKEN (RIBF)
Richard Johnson | BCS (Industry)
Jongwon Kim | IBS (RISP)
Jangyoul Kim | IBS (RISP)
Itaru Shimizu | Tohoku University (IsoDAR)
Yuji Matsubara | SHI (Industry)
Toshinori Mitsumoto | SHI (Industry)
Hiroki Okuno | RIKEN (RIBF)
Hiroshi Tsutsui | SHI (Industry)

## Slide 3: Goals of Workshop
Question 1
  Is there a realistic need for high-power (>100 kW) cyclotrons of K > 160 for q/A ≤ 0.5?
Question 2
  Can we establish the actual requirements for each of the applications?
Question 3
  Can these machines be built? And more importantly, under what circumstances would vendors be interested in bidding and signing contracts to develop and build them?
Question 4
  Can we begin to think of possible collaborations amongst the interested Laboratories and Universities to share ideas, and jointly develop plans towards furthering the experiments and projects built around these high-power cyclotrons?

## Slide 4: Goals
Question 1:
  Is there a realistic need for high-power (>100 kW) cyclotrons of K > 160 for q/A ≤ 0.5?
Response:
Three cases were made:
IsoDAR (Sterile neutrino search at KamLAND)
RISP (Radioactive Ion Beam facility, Daejon, Korea)
RIBF (Uranium intensity upgrade at RIKEN)
Speculation regarding other potential applications

## Slide 5: IsoDAR
Baseline design:
  H2+ (reduced space charge, higher currents)
  5 mA (10 mA protons on target)
  60 MeV/A (Optimizes neutron production in Be target)
Option (not considered at present):
  Deuteron 40 MeV/A
    Activation is a very serious problem in the low-background KamLAND environment
      Beam loss leads to high-energy neutrons that are very difficult to shield
    Advantages: better size, easier access to KamLAND, lower cost
    Problem: machine is no longer the DAEdALUS* injector
      But is demonstrator of concepts
*DAEdALUS concept has IsoDAR cyclotron as the injector
to a RIKEN-like SRC for 800 MeV/A H2+ beams

## Slide 6: RISP
Baseline is 70 MeV proton, 1 mA
Change to q/A = 0.5, 40 MeV/A presents attractive options
  Greater flexibility in research possibilities
    H2+ (protons), deuterons, He++ easily interchangeable
  Cost is higher
MORE IMPORTANT is time!
  2020 timetable for installation completion
    Estimate extra year to develop new q/A = 0.5 vs existing proton machines
    60 MeV/A machine might take an additional 6 months
  Whatever option selected, want to sign cyclotron contract soon!
Cost comparison*: (NOTE difference between “cost” and “price”)
  70 MeV proton ~$16M (cost) [$17M price]
  40 MeV/A q/A = 0.5 ~ $20-22M (cost) [not showstopper for RISP]
  60 MeV/A q/A = 0.5 ~ $24-30M (cost)
  * Numbers from Luciano

## Slide 7: RIBF
Intensity upgrade for existing cyclotron chain
  Eliminate one stripping stage
    Gain: factor of 5 to 10
  All ions, especially U35+ q/A > 1/7
Separated sector cyclotron, superconducting coils
  3.2 T maximum field
  48 MeV/A
Would compact cyclotron (same specs as IsoDAR) be useful in injection?
  Probably not
  RF may be problem for lower q/A (turn separation)

## Slide 8: Other Applications:
ADS
  Cyclotron community not geared to ADS type project, linac community better organized, politically more coordinated
  Cyclotron option more cost-competitive
  Lower intensity, but better platform for ADS application development
  DAEdALUS type configuration could be excellent prototype
  How to break into this field?

## Slide 9: Other Applications
IsoDAR-type cyclotron for medical isotope production?
  Biggest impediment is cost for much larger machine
    Very competitive market
  Higher currents produce greater yields
    BUT: higher power presents serious target problems
  Reliability argument indicates better option is several smaller machines so maintenance downtime can be staggered

## Slide 10: Goals
Question 2:
Can we establish the actual requirements for each of the applications?

## Slide 11: IsoDAR
Baseline
  Beam: H2+
  Current: 5 mA
  Energy: 60 MeV/a
  Extraction: conventional septum
    With “pre-septum” stripper
  Injection: Conventional LEBT with spiral inflector
    RFQ buncher reduces risk of achieving baseline current

## Slide 12: RISP
Initial Baseline:
  Beam: protons
  Current: 1 mA
  Energy: 70 MeV
Proposed New Baseline:
  Beam: deuterons, H2+, He++
  Current: 1 mA
  Energy: 40 MeV/A (maybe 60?)
  conventional source, LEBT are OK

## Slide 13
RIB (RIKEN)
New FRC (Superconducting)
Spec. of Super-FRC | 
K-value | 2220 MeV
Vel. gain | 2.06
Injection energy | 10.8 MeV/u
Extraction energy | 48.0 MeV/u
Accel. frequency | 73 MHz
Harmonics | 18
Injection radius | 1.775 m
Extraction radius | 3.65 m
Spec. of sector magnet | 
Number of sector | 4
Weight/sector | 1200 t
Pole gap | 180 mm
Magneto motif force | 1.62 MA
Bmsax on trajectory | 3.2 T
NC trim coils | 20 pairs

## Slide 14: Commonalities
IsoDAR and RISP could have very similar machines
  Great opportunities for phased development and commissioning
RIKEN could benefit from component or subsystem developments
  e.g. Vacuum requirements similar
Activation studies important for all

## Slide 15: Staging and Commissioning
A q/A = 0.5 RISP cyclotron is (most likely) a lower-power, lower-energy analog of the IsoDAR machine
  Schedules: RISP timeline is a year or two ahead of IsoDAR
Commissioning of RISP machine at ~1 mA provides valuable information for design of IsoDAR machine

## Slide 16: Commissioning Thoughts
Commissioning RISP machine with H2+ (instead of deuterons) reduces activation
RISP machine commissioning provides important data for scaling up to IsoDAR’s higher energies and currents
  Evaluation of controlled and uncontrolled losses
  Assessment of reliability, for fine-tuning engineering design

## Slide 17: Goals
Question 3:
Can these machines be built? And more importantly, under what circumstances would vendors be interested in bidding and signing contracts to develop and build them?

## Slide 18: IBA
Has mature design for K = 70 machine
  Delivering third machine in 2015
  Multi-ion option available, though single-ion is easier
K ≥ 160?
  Might be interested in studying critical “elements” (subsystems)
    space charge
    activation
    RF
  Building whole machine ?
    Difficult to commit
    How many would it take?
      depends on cost, resource needs
      High commitment in resources required for development
        Would need to see a good market potential

## Slide 19: Best Cyclotron Systems
Installed K=70 at Legnaro
  H-, 700 mA
K ≥ 160?
  Whole new engineering effort
  Many difficult problems
    Especially for IsoDAR’s 5 mA (600 kW)
  Would be willing to participate in non-competitive R&D efforts, and cooperative partnerships

## Slide 20: Sumitomo
Extensive experience in building cyclotrons
  7 MeV PET to K = 2600 SRC at RIKEN
High-current designs:
  30 MeV H- for BNCT operating at KURRI
    1.5 mA demonstrated, design 2 mA
  40 MeV deuteron (20 MeV/A, K = 80) for 99Mo production
    Design concept, 2 mA goal
K ≥ 160?
  99Mo cyclotron would be good base to scale from
    Source, LEBT, injection for deuterons all relevant for 1 mA RISP
      5 mA would need considerable effort though
  Willingness to respond to tender from RISP/IsoDAR?
    Depends…
      Many factors to consider with new, larger machine: mill beds, transportation, …
      Also assembly (factory or on site) and commissioning strategies
    As with RIKEN projects, preferable would be to build to design specifications, with no performance guarantee

## Slide 21: RIKEN
Suggestion to base design for compact q/A=0.5 machine on FRC
  K = 700, scaling down to K=240 reduces size
  Compact: 4-sector design reduces steel weight (possibly by factor of 2)
    Could reduce access/assembly problems at KamLAND
      Smaller pieces
  Injection could be problem
    Maybe a higher-energy RFQ system would work?

## Slide 22: Observation
Up to a certain size, usual choice is a single vendor.
Above this, machines are usually built by consortia.
  E.g. RIKEN SRC, HIMAC, SNS (Oak Ridge, USA)
Could high-current, K>160 cyclotron be above this threshold?

## Slide 23: Goals
Question 4:
Can we begin to think of possible collaborations amongst the interested Laboratories and Universities to share ideas, and jointly develop plans towards furthering the experiments and projects built around these high-power cyclotrons?

## Slide 24: Observation
The science represented at this Workshop covers very different fields
  Collaboration on the scientific front is not likely to be of benefit
But all “customers” could benefit from technical collaborations to obtain these challenging machines!

## Slide 25: Possible Scenario
Physics Design performed by collaboration of laboratories/universities
This produces detailed specifications for cyclotrons
  Designed to meet performance goals of each project
  Aim to maximize commonality of subsystems
These specifications form the Tenders for each of the Projects
Industry can respond to these Tenders by also forming consortia for subsystems

## Slide 26: Physics Design: International collaboration plan
Beam optics (PSI, INFN..., RISP)
  isochronous fields
  central region to accept 1-5 mA
  extraction with the removal of beam halo
  estimation on beam losses depending on loss mechanism
RF cavity (PSI, INFN…, RISP)
  Cavity design for high voltage slope
  Design to lessen activation issue
Parameters applicable to either 40 or 60 MeV/A, q/A = 0.5

## Slide 27: Industrial Participation
Physics design forms basis for Tenders
Industry response possibilities:
  Sole vendor
  Consortium of vendors with shared responsibilities
    One vendor leads, subcontracts others
  Can propose other technical options beyond “physics design”

## Slide 28: Summary
Excellent exchanges of ideas and information
High level of interest in high-intensity cyclotrons
Groundwork laid for rapid progress in collaborations and designs
Our sincere thanks to Hiroki Okuno and RIKEN for hosting this most interesting workshop!