## Slide 1
The IsoDAR Cyclotron
Luciano Calabretta,
INFN-LNS, Catania, Italy
…or a compact cyclotron to accelerate
H2+, Deuteron+,- and fully stripped light ions

## Slide 2: Accelerator Requirements
IsoDAR
  Energy: Efficient production of neutrons in beryllium target (desired reaction is 7Li(n,g)8Li)
  40÷80 MeV
  Beam species: beam on target: protons or deuterons
  Beam intensity: calculated to provide statistics in 5 year experiment – 10 mA
  Time structure: No timing requirements, so want greatest possible on-time (for statistics)

## Slide 3: Problems to deliver10 mA proton with Cyclotrons: - Injection
Central region: space-charge blowup
  Energy is low (~ 30 ÷ 80 keV)
  Current is high (~ x5 higher than today values)
  Electrostatic forces hard to contain
High “Perveance” value:
  (measure of space-charge forces)
  K ∝ I (q/m) (bg)-3

## Slide 4
Proposed solution:
Acceleration of H2+ ions
to produce
high intensity proton beam
  The Generalized Perveance measures the space charge effect and it is defined by the Reiser’s formula:
Two protons for every ion (1 emA = 2 pmA).
Perveance of 5 emA H2+ at 35 keV/amu same as 2 emA of 30 keV protons
Extraction with stripping foil may be is feasible. It requires a high-acceptance extraction channel but not a clean turn separation.
May be there is a problem with the life time of stripper foil
axial injection of 2 emA protons at 30 keV is an upper limit

## Slide 5
e-
e-
D-
  The Generalized Perveance measures the space charge effect and it is defined by the Reiser’s formula:
1 Deuteron for every ion.
Perveance of 1 emA D+ or D- at 35 keV/amu same as 0.4 emA of 30 keV protons
Use of D+ is convenient to minimize the beam losses along the acceleration and due to interaction with the residual gas!
axial injection of 2 emA protons at 30 keV is an upper limit
Regarding space charge acceleration of D+ ions
is similar to accelerate H2+
p+ n
D+
Use of D- is convenient for the extraction! But vacuum problems!
A Cyclotron for H2+ is usable for D+ and also for D-

## Slide 6
Electrostatic Deflectors
This is one of the two coils of ISODAR
MC2
Equilibrium Orbit
MC1
RF Cavity
extraction trajectory for H2+ or D+
Despite we extract just one beam,
Anyway 4 extraction channel are drilled in the iron yoke to maintain the symmetry of the magnetic field!
The RF Cavity in this layout have an angular width of 30°, in the final project could be larger, about 40÷44°,

## Slide 7
DAEδALUS Injector Cyclotron: Peak current 5 mA H2+ , <I>= 1mA
arXiv.org > physics > arXiv:1207.4895
Einj | 35 AkeV | Emax | 61.7 AMeV
B0 | 1.075 T | <B> at Rext | 1.166 T
<Rinj> | 51.58 mm | <Rext> | 2000 mm
N. Sectors | 4 | Hill width | 25.5° ÷ 36.5°
Valley gap | 1800 mm | Hill gap | 100 mm
Diameter | 6240 mm | Full height | 2700 mm
N. Cavities | 4 | Cavities λ/2 | Double gap
RF Harmonic | 4th | RF frequency | 32.8 MHz
Acc. Voltage | 70  250 kV | Power/cavity | <160 kW
Coil size | 200x250 mm2 | Current density | 3.17 A/mm2
Equilibrium Orbit
IsoDAR cyclotron
Ipeak= <I> =5 mA H2+
up to 44°!

## Slide 8
Stripper foil
emerging
protons
H2+ beam
electrons
catcher
If B=0.4 T Re=4.5 mm
Beam Extraction of H2+ from IsoDar Cyclotron by stripper
is not convenient because the beam size is larger than > 10 mm!
Electrons are the main source of stripper damage. In fact, 600 kW beam @ 60 AMeV on a stripper foil 0.2 mg/cm2 thick means < 4 W due to nuclear interaction, while the electrons removed by the strippers have a full power of 600 kW*Me/MH2=600/(2*1826)=164 W !
Electrons have to be stopped before they strike the stripper!
Center of Cyclotron
For D- beam with maximum current of 1 mA, maximum power on the stripper foil is about 66 W!
It is anyway quite high!
For acceleration of D- the main drawback is the beam losses during acceleration and activation of the cyclotron!
Notes: Break
Comunque, a parita di energia di fascio incidente ed a parita di protoni estratti diciamo 100 protoni estratti, nel caso di H2+ abbiamo strippato 50 elettroni, mentre nel caso di H- ne abbiamo strippato 200! é l'energia degli elettroni che danneggia primariamente lo stripper. Un'altra considerazione per sapere quanto vale l'energia degli elettroni strippati. Per un fascio di 100 MeV di H- l'energia di ciascun elettrone strippato è di 1/2000 quindi di 50 keV, pertanto l'energia dei due elettroni strippati è di 100 keV. Nel caso di H2+ da 100 MeV/amu (protoni finali sempre da 100 MeV), l'energia dell'elettrone strippato è ancora di 50 keV, ma a fronte di estrarre due protoni da 100 MeV. In potenza se estraiamo un fascio di protoni da 100 kW accelerati con H-, la potenza degli elettroni strippati è di 100W, mentre se lo abbiamo accelerato con H2+ la potenza degli elettroni strippati è di solo 25 W!

## Slide 9
Beam Extraction of D- from IsoDar Cyclotron by stripper
seems feasible!
But I don’t like D- for the beam losses during acceleration!
Electrons are the main source of stripper damage. In fact, 120 kW beam @ 60 AMeV 1 mA on a stripper foil 0.2 mg/cm2 thick means < 0.2 W due to nuclear interaction, while the electrons removed by stripper have a full power of 120 kW*2Me/MH2=120/(1826)=66 W !
stripping process for H-:
H- =(p+e+e)  p, e, e
is a two steps process:
(p+e+e) H + e  p, e, e
stripping process for D- :
D- =(D+e+e)  D+ , e, e
is a two steps process:
(D+ +e+e) D, e  D+, e, e
stripping process for H2+:
H2+ =(p+p+e)  p, p, e
is a one step process:
Notes: Break
Comunque, a parita di energia di fascio incidente ed a parita di protoni estratti diciamo 100 protoni estratti, nel caso di H2+ abbiamo strippato 50 elettroni, mentre nel caso di H- ne abbiamo strippato 200! é l'energia degli elettroni che danneggia primariamente lo stripper. Un'altra considerazione per sapere quanto vale l'energia degli elettroni strippati. Per un fascio di 100 MeV di H- l'energia di ciascun elettrone strippato è di 1/2000 quindi di 50 keV, pertanto l'energia dei due elettroni strippati è di 100 keV. Nel caso di H2+ da 100 MeV/amu (protoni finali sempre da 100 MeV), l'energia dell'elettrone strippato è ancora di 50 keV, ma a fronte di estrarre due protoni da 100 MeV. In potenza se estraiamo un fascio di protoni da 100 kW accelerati con H-, la potenza degli elettroni strippati è di 100W, mentre se lo abbiamo accelerato con H2+ la potenza degli elettroni strippati è di solo 25 W!

## Slide 10
Vertical beam size vs. turns number for different beam currents
Beam size acceptable! Initial normalized emittance is 0.6 p mm.mrad!
Realistic normalized beam emittance inside the cyclotron 1 p mm.mrad.
1 MeV/n
61.7 MeV/n
Beam dynamics in DAEδALUS Injector Cyclotron
Simulation made by J. Yang and A. Adelman @ PSI, using OPAL code.
rms
Beam size rms

## Slide 11
The first turn start at 1 AMeV and the rms normalized emittance in both radial and vertical plane was 0.6 p mm.mrad
The phase acceptance and the energy spread are ±10° RF and ±0.2%
Rms Beam size along the acceleration path (on the left)
and rms beam size along the last two turns (on the rigth)
The first turn start at 1 AMeV

## Slide 12
E=60
AMeV
E=40
AMeV
Inter-turn separation vs. <R> just due to RF cavity acceleration!
A first harmonic precession is able to increase the inter-turn separation at extraction radius up to 20 mm!

## Slide 13
Beam dynamics in DAEδALUS Injector Cyclotron
Deflector septum
0.5 mm width
Be careful! The rms beam size could be misleading!
Extraction efficiency 99.98%, if beam power is 600 kW on the septum 120 W!
Beam injection
14 mm
20 mm

## Slide 14
<R> [cm]
E=40 AMeV  <R>=163 cm ; E=60 AMeV  <R>=199 cm

## Slide 15
The vertical beam halo is ±10 cm, at this point
Stripper at Teta=0°
If stripper position is between -65° and -10 °
spiral code is not able to evaluate the trajectory and beam envelope. Simulation made with OPERA
Extraction process for H2+
Safe!

## Slide 17
May be also for D+ beam could be possible to protect the deflector septum.
May be the beam envelope of the removed halo could be also smaller in vertical, but we need to perform additional simulation.

## Slide 19
Cyclotron Center
220 cm
252 cm
31 cm
hill
yoke
hill upper part
skirt valley
Outer radius of pole  220 cm
Inner radius of yoke  252 cm
Inner radis of coil  225 cm
Outer radius of coil 250 cm
Distance yoke surface below the coil from median plane 31 cm
Coil distance from median plane  10.5 cm.

## Slide 20: RF Cavity shape and surface H field
Courtesy by Michel Abs

## Slide 21: E field
Courtesy by Michel Abs

## Slide 22
Coupling to the cavity
It is proposed to couple the power in the median plane via a quarter wave resonant line
The voltage on the RF tube is independent of the load (beam loading)
No fine tuning is needed on the amp side (reactive currents flow to the cavity)
Leaves the bottom of the cyclotron free to place ion source and vacuum pumps.
Clearly the cheapest option

## Slide 23: Dee voltage law vs radius
Chart: Dee voltage vs radius @ 100kW/ cavity (70% of theorethical Q)
| 100.0 | 400.0 | 700.0 | 1000.0 | 1300.0 | 1600.0 | 1900.0
E gain/gap (keV) | 61.6146 | 72.8329 | 83.2746 | 102.6046 | 132.7215 | 162.2344 | 185.0163
Vdee peak(kV) | 78.0106 | 79.5639 | 87.9345 | 111.1478 | 139.3663 | 170.2598 | 194.1635
Courtesy by Michel Abs
Scaling Voltage up to 240 kV
Power increase up to 160 kW.
Beam loading per cavity 150kW

## Slide 24: Main mechanical parameters
Cavity height: 1800mm
Radial extension: 2100mm
Liner angular aperture: 38°
Dee angle: 34°
Inner Dee vertical gap: 50mm (100mm in the outer radius for deflector location)
Dee plate thickness: 20mm
Dee stems dia.(4/ Dee)= 200/120mm
Dee stiffener: 50mm width
Courtesy by Michel Abs
46°
42°

## Slide 25: Electrical parameters
Unloaded Q= 9540 (theoretical)
Main mode resonance frequency: 32.7MHz
Hmax: 6900A/m
Surface resistance: 1.53mOhms
Max surface dissipation: 3.6W/cm²
Courtesy by Michel Abs

## Slide 26
Chart: Beam losses vs. R (H2+, I=5 mA), Vacuum 1.33*10-6 Pa 40% Hidrogen, 60% Nitrogen
*RF Voltage constant=225 kV  109 turns
Vacuum is challenging!
Cryogenic panel and/or NEG panel are mandatory!

## Slide 27
Chart: Beam losses vs. R (D-, I=1 mA), Vacuum 1.33*10^-6 Pa 40% Hidrogen, 60% Nitrogen
80
60
40
20
*RF Voltage constant=225 kV  109 turns
Vacuum is challenging!
Cryogenic panel and/or NEG panel are mandatory!

## Slide 28
Chart: Beam losses vs. R (D+, I=1 mA), Vacuum 1.33*10-4 Pa 40% Hidrogen, 60% Nitrogen
80
60
40
20
*RF Voltage constant=225 kV  109 turns
Vacuum is not serious!

## Slide 29: Ion Source, Injection Tests
How much H2+ can we get from a proton source? (VIS Catania)
How much can we capture in central region?
Tests performed at Best Cyclotron Systems development Lab, Vancouver BC, Summer 2014
Beam Stop

## Slide 30: VIS Source Allison emittance scanner collimator, beamstop

## Slide 31: Observations

## Slide 32
Summary of tests at BEST site in Vancouver
Transport maximum 10 mA of H2+ to cyclotron, focus beam at entrance to spiral inflector.
  Size: 8 mm (2-rms)
  Emittance: 1.2 π-mm-mrad (4-rms, normalized, 86% of beam)
Transport 95% of beam through spiral inflector
Accelerate 100 µA for four turns in test cyclotron, but RF Voltage <60 kV
Conclusion: Have good simulation tools in hand
Conclusion: Need more current.
How? Either better source or higher bunching efficiency
Pursue both:
  Build new ion source (multicusp)
  Develop RFQ direct cyclotron injection design

## Slide 33: Results to Date
√ Characterize VIS source for H2+
- Max current : 12 mA… we need much more!
  - Emittance : ~ Twice larger than expected
√ Test beam line for separation of protons/H2+~OK
Inflection/capture in test cyclotron :
  RF Voltage <60 kV, instead of the 70 kV required!

## Slide 34
The main difference between the Test site used in Vancouver and IsoDAR cyclotron is the number of RF cavities ( 4 for IsoDAR instead of 2 in the test site) and the Harmonic mode (4th for IsoDAR instead of 6th for the test stand). The injection energy was 60 keV!
The test of the spiral inflector (15 mm gap) demonstrate that it works with +/-10 kV, when a 60 keV H2+ is injected!
Inflector tested up to +/-13.5 kV reliable!
It will be possible to inject H2+ with energy of 75-80 keV.
In this way the emittance should reduce of a factor 12-15%!

## Slide 35
The new injection beam line for H2+, including a RF buncher
Will be build by MIT

## Slide 36
Alternative option to deliver H2+ >30 mA:
RFQ in Test Beam Line

## Slide 37
What have we learned?
Existing Ion source for H2+ stay in the territory 15-30 mA;
Is convenient to work with Bunching Gain Efficiency as high as possible;
ISODAR has an acceptance phase double than PSI injector 2;
With H2+ source delivering 30 mA, a bunching efficiency >3 is convenient;
The use of Isodar cyclotron to delyver 1 mA D+ beam is feasible
For a maximum energy of 40 AMeV the extraction radius should stay at 1.63 m, 15% smaller than IsoDAR cyclotron;
Many problem of IsoDAR cyclotron are relaxed!

## Slide 38
The use of Isodar cyclotron to delyver 1 mA D+ beam is feasible
For a maximum energy of 40 AMeV the extraction radius should stay at 1.63 m, 15% smaller than IsoDAR cyclotron;
Many problem of IsoDAR cyclotron are relaxed!
The main advise to use IsoDAR cyclotron to accelerate Deuteron
concerns the activation of the cyclotron itself
and in particular of the RF Cavities copper made.
May be the activation could be reduced covering all the surfaces of the median plane with 5-10 mm thick graphite layer or Aluminum!
This layer prevent the production of bad radioisotope of cupper.

## Slide 40
Thanks for your attention!

## Slide 41
Range of 40 MeV proton in Uranium target 1.85 mm
Range of 40 MeV Deuteron in Uranium target  1.18 mm
Range of 40 AMeV Deuteron in Uranium target  3.77 mm
40 AMeV
60 AMeV
Gain a factor 1.6 due to cross section, + a factor 2 for double range, + a x factor due to the secondary neutron production and the fragments are more neutron rich!

## Slide 42
D @ 40 MeV
D @ 80 MeV
500 microA  40 kW
p @ 40 MeV
500 microA  20 kW
p @ 80 MeV
Range 3.77 mm
Range 1.85 mm