## Slide 1: Cyclone 70
IBA Radiopharma’s high energy, high current cyclotron

## Slide 2: Cyclone 70 = 2 models
Cyclone 70 XP  research + production solution
  Proton (H-)
  Deutons
  Alpha
  HH+
Cyclone 70P  production solution (Sr82 production)
  Proton only (H-)

## Slide 3: Main characteristics of Cyclone 70
Beam exit | 2 exits | 2 x 3 ports (*)
Cyclotron weight | 145 Tons | On 4 pillars
radius | 1240 (pole) | 1910 mm (overall)
Vacuum system | Cryo pumps | Clean vacuum cyclotron
 | Turbo pumps | Clean vacuum ion source
Electrical load | 60 kW | Stand-by
 | < 250 kW | Full beam /2 Beam lines (%)
(two beam lines) | ~25 kW | Load included in (%)
Cooling load | < 200 kW | Full beam, water chiller
Extracted beams ~1.23 T.m
RF | 
Frequency | 30 (xp) ot 58 (p) MHz
Dee’s voltage | Mean 65 kV
Power - cavity | 22 kW (2 cavities)
Power – full beam | 56 kW (beam load)
NB: loads of details at cyclotrons & ECPM conferences as from 2007

## Slide 4: Current status – multi-particle
70 MeV / 750 µA proton - World record established 10/2010

## Slide 5: Current status of the proton only
Zevacor project being shipped soon, CDMN under mapping this summer
20 months from order to shipment of 1st Unit

## Slide 6: Overview: from source to extraction

## Slide 7: Sources
H-/D- => multicusp ion source from D-pace
q/M=0.5 => supernanogan from Pantechnik
  Capacity 10mA H-, superbright emittance
  30 kV platform
  Easy maintenance (one back plate with 4 filaments)
  Differential pumping system for high vaccum level

## Slide 8: Injection Line overview
Multi-particle machine
solenoid
90°bend
Quad triplet
solenoid
solenoid
Buncher
« good match »: particle accepted for more than 50 turns)
Notes: Injection efficiency: 10-20%
Acceptance for H- 43-22 pi mm mrad
For He: 23 pi mm mrad

## Slide 9: Injection line overview
H- proton source and injection (same as high current Cyclone 30 HC)
Proton only: simplified design

## Slide 10: Injection line overview
Proton only, cont’d

## Slide 11: Magnet

## Slide 12: Magnet
Multi-particle machine

## Slide 13: Magnet : compromise for all particle
Computation, CA Design and engineering

## Slide 14: Magnet
Yokes/flux returns in 1 piece
No more compensation coil
No more pole extension (He++ focalisation)
Optimisation of pole thickness and profile
Gap increasing (30mm ->40mm)
Main differences between proton only and multi-particle
Why?
  Assembly optimised
  Better vacuum level
  Reduce power consumption (main coil + harmonic coils)
  Improve vacuum pumping

## Slide 15: RF system
Cyclone 70Xp - ~30 MHz in H2 for protons, H4 for M/Q=2
Different stem configurations have been tested in order to find the best compromise between mechanical/RF/beam parameters.
Large number of turns for protons; possible higher losses in acceleration
Chart: Radius
| 120 | 220 | 320 | 420 | 520 | 620 | 720 | 820 | 920 | 1020 | 1120
V dee (kV peak) | 65 | 64.7958 | 64.1832 | 62.6178 | 60.9162 | 59.0785 | 56.9686 | 55.199 | 54.1099 | 53.6335 | 53.4293
Energy gain/gap (keV) | 30.5602 | 30.7644 | 31.377 | 31.0366 | 30.4921 | 29.6754 | 28.5864 | 27.3613 | 26.4764 | 26 | 25.2513
beam lost/ 100mm radius increase (arbitrary scale) | 108.4841 | 93.0308 | 87.6812 | 86.6473 | 87.5194 | 90.0016 | 93.8406 | 98.0209 | 101.4105 | 105.0086 | 0
Arronax case (H2)
V Dee centre: 65kV
#of turns: 625
P Diss.: 20kW (measured)

## Slide 16
Harmonic 2 for proton acceleration – 30Mhz (compromize with other particles)
Inductive coupling (in the pit)
RF system
Cyclone 70Xp - H2 for protons, H4 for M/Q=2

## Slide 17: RF system – proton only
Protons on 4th harmonic
Straight pillar 110mm (better rigidity)
Vcentre: 50kV
P diss: 32.7kW
#of turns: 625=>321
Chart: Radius
| 120 | 220 | 320 | 420 | 520 | 620 | 720 | 820 | 920 | 1020 | 1120
V Dee (kV peak) | 55 | 54.5812 | 51.8591 | 48.9277 | 48.7881 | 52.1383 | 57.5127 | 63.3058 | 68.5406 | 72.5888 | 75.5203
Energy gain/gap | 42.7157 | 44.1815 | 43.4137 | 41.6688 | 41.8782 | 44.9492 | 49.6256 | 54.2322 | 58.2107 | 59.1878 | 62.8173
Beam losses | 76.5692 | 65.9968 | 64.3325 | 63.8098 | 60.6794 | 55.5027 | 50.5891 | 46.9555 | 45.3296 | 44.1263 | 0
RF H2->H4 allow to gain ~4% of transmission
Notes: Beam losses: 59% (of H2 cavities)

## Slide 18: RF system – proton only, while we’re busy with it…
Cyclone 30HC amplifier
Coupling in median plane
  no asymmetry between cavities
  low amplifier and coupler dissipation at 80 kW total RF (100 kW available)
only one cavity tuning at the opposite side of the coupler.
Direct FPA coupling to Dee: more stable system

## Slide 19: Extraction systems
Electrostatic deflector is coupled to pole extensions for optics correction
We burned some of these during commissioning despite the cooled pre-septum (less turn separation than IsoDAR, so we cannot remove halo)
Electrostatic deflector
Notes: IsoDAR: 300kW of RF… we have less than a third of IsoDAR power ang are more compact.

## Slide 20: Extraction systems
Dual stripping shaft and permanent radial probe