## Slide 1: Vernier Analysis Tutorial
Spin Fest 2016
Mike Beaumier, PhD
University of California, Riverside

## Slide 2: What is the Vernier Analysis?
The Vernier Analysis seeks to measure the luminosity of RHIC’s beams at the PHENIX interaction region.
This luminosity is characterized by the overall event rate observed by PHENIX’s luminosity monitor (), the cross section of these events () and BBC efficiency ():
The Vernier Analysis requires a special data set taken during a Vernier Scan.
The Vernier Scan allows us to extract parameters related to the beam geometry to calculate luminosity from first principals.

## Slide 3: Why do we need to know ?
Many PHENIX analyses calculate the invariant cross section, with respect to particle production:
Without a direct measurement of luminosity, we must rely on predictions based on p+p collisions and CAD measurements
Knowing , , and is useful for calibrating detector efficiencies, geometric acceptances, and overall calibration of the BBC as a luminosity monitor

## Slide 4: What is the Vernier Scan?
Blue Beam
Yellow Beam
Beam Displacement
BBC Rate
One beam is swept transversely across another. Correlating the displacement to the BBC rate produces the transverse beam profile.

## Slide 5: Parameters, Data Sources
Run Scalers, Beam Position Monitors, Wall Current Monitors
Parameterize beam geometry for blue and yellow beams (, , )
Maximum collision rate of the beams ()
ZDC, BBC, Simulation
Beta-squeeze parameter () and the crossing angle between the beams ()
Luminosity correction factors (, )
Run Scalers
Multiple collisions rate ()
Efficiency of the BBC detector ()
Bunch crossing frequency of the beams ()
Number of bunches in the beams ()
Wall Current Monitors, Direct-Current Current Transformers
Total beam current, and beam ions per bunch (, )

## Slide 6: Calculating Luminosity
Transverse bunch distributions in the x and y directions are implicitly functions of z, due to the beam squeezing effect and crossing angle (discussed in context of hourglass correction)

## Slide 7: Extracting the Transverse Beam Profile

## Slide 8: Run Scalers
Trigger Scaler | Description
“BBCLL1(>0 tubes) novertexcut” (BBC wide) | Fires any time there is a coincidence of the BBC North and South within a prescribed time window
“BBCLL1(>0 tubes)” (BBC narrow) | Same as novertex cut, but with an online vertex cut of approximately +/- 30 cm
“ZDCLL1wide” (ZDC wide) | Fires any time there is a coincidence of the ZDC north and South within a prescribed time window
“CLOCK” | Fires once every beam clock count (once per bunch crossing)
The GL1-1P scalers must be specially programmed into the GL1-1P boards. These scalers record the number of live triggers for each scaler, and sum them. The sum is read out each recorded event, and the counter resets

## Slide 9: The BBC Rate
Events are ordered in time by summing every 1000 events. The BBC wide scaler is divided by the clock scaler for each bin to obtain the BBC rate

## Slide 10: The BBC Rate
Note the obvious stepped distribution of the BBC rate. Each step corresponds to the BBC rate associated with a fixed beam displacement.

## Slide 11
Obtaining Beam Positions
z
PHENIX Interaction
Region, Coordinate System
BPM
Sector 8 Plane
Use measurements at BPM7 and BPM8 to produce intersection point at IR plane of blue, yellow beams.
Then, once intersection points are known, calculate distance between beams, s, at the IR plane.
x
y
Blue beam
Yellow beam
s
BPM
Sector 7 Plane

## Slide 12: Monitoring Beam Position
While BPMs do not necessarily give an accurate position for each beam individually, they can be used to calculate the separation between the beams
Beam Position Monitor

## Slide 13: Beam Width Fit
The beam displacements are correlated to the related rates, and the distributions are fit with a Gaussian. The width of the Gaussian gives a measurement of the beam width for the horizontal and vertical dimensions of the beam.

## Slide 14: Beam Width Fit
A simultaneous Gaussian fit in x and y provides the ‘actual’ value for the beam width in the transverse directions.
0.0254 mm
0.0251 mm
Simultaneous Beam Width
X Displacement
Y Displacement

## Slide 15: Beam Ion Population

## Slide 16
Wall Current Monitor
Direct-Current Current Transformer
The wall current monitor offers sub-beam clock current timing, and is sensitive to beam bunching, but is less accurate than the DCCT
The DCCT is sensitive to the overall beam population, and can be used to correct the readout of the WCM

## Slide 17: Calibrating the WCM with DCCT

## Slide 18: Calibrating the WCM with DCCT
The calibration may be done in ‘real time’
Calibration constant calculated, applied when DCCT + WCM data available simultaneously
Distribution of calibration can be studied
Blue Beam Calibration
Yellow Beam Calibration

## Slide 19: Beam Ion Population Per Bunch

## Slide 20: WCM and Luminosity Loss
Recall that
Product vs time can give us % luminosity loss due to beam ion loss during Vernier scan.
~1% loss for whole scan.

## Slide 21: BBC Efficiency,

## Slide 22: BBC Efficiency,
The BBCs are geometrically limited, and additionally have an associated trigger efficiency.
Beam collisions happen more frequently than the BBC’s recorded rate!
Geometric acceptance:
144.34 - d
144.34 + d
BBC S
BBC N
10 cm

## Slide 23: Using the ZDC To Calculate
Solid angle of BBC plotted for all possible z-vertices for the BBC and ZDC
Relatively flat geometric acceptance of the ZDC over the range of the BBC allows us to use it to calculate the efficiency of the BBC
Z-Vertex
Solid Angle “As Seen From Vertex”
BBC
ZDC
Solid Angle “As Seen From Vertex”
Z-Vertex

## Slide 24: BBC Wide&Narrow vs BBC Wide
Events are binned in z-vertex for coincidences of the BBC wide AND BBC narrow triggers (left) vs BBC wide (right). Taking the bin-by-bin ratio of these distribution shows the trigger acceptance of the BBC narrow trigger.

## Slide 25: BBC Trigger Acceptance
Creating the trigger acceptance plot shows a clear turn on where there is maximum overlap between BBC wide and narrow triggered events. The absolute value of the derivative of the acceptance can be used to pinpoint the online vertex cut, in this case at -34.4 cm and +35.8 cm

## Slide 26: Correcting for z-Vertex Dependence
The BBC response has a z-dependence, more so than the ZDC. This is corrected for by creating a histogram in z-vertex for events firing the BBC wide and ZDC wide triggers, and events which fire the ZDC wide trigger. A bin-by-bin ratio is taken.

## Slide 27: Correcting for z-Vertex Dependence
A quadratic function is fit to the resulting profile, which gives the z-vertex correction for the BBC. The BBC wide distribution is integrated over the nominal z-vertex cut region, and divided by the total yield. The z-vertex correction is applied bin-by-bin. The result is the efficiency, which for Run 359711 is about 0.43

## Slide 28: The Hourglass Effect
Simulations to determine and

## Slide 29: What is the Hourglass Effect?
The hourglass effect describes the z-vertex profile of events generated for collisions with displaced beams
The squeezing and crossing increases luminosity, so we must account for it in our model
causes a split in the z-vertex distribution, causes asymmetry in peaks, causes scaling

## Slide 30: Crossing Angle Transformation

## Slide 31: Transformation

## Slide 32: Real Beam Profiles
The blue and yellow z-distributions are recovered directly from the data
The distributions are fit with a triple-Gaussian.

## Slide 33: Simulating ZDC z-vertex Profile

## Slide 34: Convergence of Simulation

## Slide 35: Simulation Results

## Slide 36: Putting it All Together
With, and recovered, luminosity can be estimated.
  Luminosity with and without and may be calculated to obtain overall corrective factor ()
Luminosity is then calculated directly from the data:

## Slide 37: Thank you!