## Slide 1
An empirical method for improving the XMM-Newton/EPIC-pn RMF and ARFs
Konrad Dennerl - Max Planck Institute for Extraterrestrial Physics – Garching - Germany

## Slide 2
Chandra ACIS-S3
Swift XRT
XMM RGS
XMM MOS1
XMM PN
± 20%
Plucinsky et al. 2017 (A&A 597)
Suzaku XIS

## Slide 3
Example: XMM/EPIC-pn, simultaneous fit to RXJ 1856 and 1E0102 in three filters each,
using the same model spectrum for each source, with no normalization between the filters
Warning: ARF adjustments alone may be dangerous !
The apparent excess in residuals below 0.4 keV could be „repaired“ by increasing the ARF at low energies ..
RXJ 1856
1E 0102
Work on the RMF refinement, however, suggests to
increase the redistribution and to decrease the ARF at low energies !

## Slide 4
EPIC pn RMF: 8.5 million matrix elements  HUGE parameter space! EPIC pn ARFs: 3 x 2067 elements  comparatively trivial
ARF: „Ancillary Response File“, RMF: „Redistribution Matrix File“
how to improve ?
General properties of the ARF and RMF
RMF @ EPIC pn: 4096 adu bins from 0.0 to 20.5 ‚keV‘ („EBOUNDS“) 2067 eV bins from 50 eV to 16 keV
2067 vector elements
2067 x 4096 = 8 446 432 matrix elements
EPIC pn:
 find appropriate RMF parameterization and try to optimize it..

## Slide 5: Model Parameters for the EPIC pn RMF

## Slide 6: Model Parameters for the EPIC pn RMF
sigma
sh_esep
sh_sig_l
shlf_rnorm
sh_rnorm
gamma,
vtherm
sh_sig_r
ecor

## Slide 7: Comparison: original and recomputed RMF @ 2.3 keV
recomputed RMF
original RMF

## Slide 8: Modeling the EPIC pn RMF at individual energies
sigma
sh_esep
sh_sig_l
sh_sig_r
shlf_rnorm
sh_rnorm
gamma,
vtherm
ecor

## Slide 9: Modeling the EPIC pn RMF at individual energies
sigma
sh_esep
sh_sig_l
shlf_rnorm
sh_rnorm
gamma,
vtherm
sh_sig_r
ecor

## Slide 10: Modeling the EPIC pn RMF at individual energies
sigma
sh_esep
sh_sig_l
shlf_rnorm
sh_rnorm
gamma,
vtherm
sh_sig_r
ecor

## Slide 11
1) Compose the RMF of (19) shaping functions SF
which are determined by shaping parameters SP:
main peak: gamma, vtherm, sigma
shoulder: sh_rnorm, sh_sigl, sh_sigr, sh_esep
shelf: shlf_rnorm, shlf_slope
escape peak: another 9 parameters
and determine deformation functions DF to model the energy dependence of each shaping parameter,
and to reproduce an existing RMF
2) Apply correction functions CF to the deformation functions DF, recompute the RMF,
use this RMF for (simultaneously) fitting X-ray spectra with spectral model functions MF (using plausible spectral model parameters MP), and compute the goodness of the fit.
Vary the correction parameters CP (and the correction functions CF) in order to maximize the goodness of the fit.
RMF refinement method
(ARF refinement comparatively trivial)
SF
DF
CF
DF

## Slide 12
Challenge: how to keep an overview (in total ~1000 parameters!)
very useful: concise graphical overview
up to 19 x 21 + 6 = 405 adjustable correction parameters in total
necessity to fix/tie/couple a subset of the correction parameters
necessity to constrain the correction functions
necessity to control the spectral fit results
RMF refinement method
19 shaping functions SF with a total of 19 shaping parameter SP;
the energy dependence of each SP is determined by a deformation function DF
the 19 DFs are computed from a total of 555 deformation parameters DP, which were derived by simultaneously fitting 39 EPIC-pn „RMF samples“ with 117 free and 438 fixed/tied parameters
19 correction functions CF, each determined by up to 21 adjustable CPs, yielding a total of 399 correction parameters CPs
spectral fits:
  1E 0102: 208 model parameters MP1, with 4 of them free + gain offset
  RXJ 1856: 3 model parameters MP2, with 1-3 of them free + gain offset
in addition for the 3 ARFs: (thick, medium, thin):
  3 x 2 adjustable parameters for C-K and O-K absorption
  up to 21 adjustable parameters for correcting the fraction of singles

## Slide 13
thick medium thin
nH == 7.25 x 1019 cm-2 kT == 62.4 eV norm == 1.58 x 105
Chandra LETG
RXJ 1856
1E 0102
Status @ IACHEC-2018

## Slide 14
thick medium thin
nH == 7.25 x 1019 cm-2 kT == 62.4 eV norm == 1.58 x 105
Chandra LETG
RXJ 1856
1E 0102
Status @ IACHEC-2018
filter dependent ARF correction | correction for carbon thickness | correction for oxygen thickness
thin | = 0 (fixed) | free
medium | = 0 (fixed) | = O_cor(thin)
thick | = 0 (fixed) | = O_cor(thin)
correction for threshold induced sensitivity drop |  | 
0.10 – 0.28 keV free | 0.28 – 1.74 keV free | 1.74 – 16.0 keV fixed
good fits (!)
ARF correction

## Slide 15
thick medium thin
nH == 7.25 x 1019 cm-2 kT == 62.4 eV norm == 1.58 x 105
Chandra LETG
RXJ 1856
1E 0102
With slight modifications of the RMF and ARF it is possible to fit simultaneously
RXJ1856, with exactly same spectral model
  EPIC pn data in all three filters
  Chandra LETG data
1E0102, with exactly same spectral model
  EPIC pn data in all three filters
Status @ IACHEC-2018

## Slide 16
software upgrade:
treat temporal dependencies as new fit parameters, individually for each shaping component
utilize parallel processing ( ≈ 10-100 times faster!)
≈ 14 000 lines of code, ~100 programs/modules/subroutines 852 RMF + ARF shaping parameters
also: various possibilities for monitoring, checks and documentation, e.g. highly compressed summary plots
Modelling temporal changes
major restructuring of the program (also opportunity to clean the code)

## Slide 17
Modelling temporal RMF changes: sample output

## Slide 18
19 RMF shaping functions
with 21 parameters each
 399 RMF parameters
21 parameters for correcting the energy dependence of
the fraction of singles
2 correction functions for the filter transmission (O and C thickness) for
each filter  6 parameters
 27 ARF parameters
426 parameters
(linear) temporal dependence of each parameter
 852 parameters
parameters can be fixed, coupled, tied, constrained,
and determined for a
given smoothness of the shaping function

## Slide 19
Modelling temporal RMF changes: sample output

## Slide 20
Modelling temporal RMF changes: shaping functions
ARF parameters
RMF parameters

## Slide 21
Modelling temporal RMF changes: shaping functions

## Slide 22
Modelling temporal RMF changes: sample output

## Slide 23
red: reduced χ2 > 1.5
green: reduced χ2 < 1.2
yellow: 1.2 ≤ reduced χ2 ≤ 1.5
Modelling temporal RMF changes: residuals

## Slide 24
Modelling temporal RMF changes: sample output

## Slide 26
Data:
1E 0102:
33 observations from rev 0375 to rev 3279
  13 x thin, 16 x medium, 4 x thick filter
  SW mode only, and only singles
  total exposure: 1.14 Ms
processed by Frank Haberl
  with xmmsas_20170330_1731-17.0.0
  using rmfgen-2.5.1, arfgen-1.93.1
RX J1856:
31 observations from rev 0427 to rev 3255
  all with thin filter
  SW mode only, and only singles
  total exposure: 2.05 Ms
processed by Frank Haberl
  with xmmsas_20160201_1833-15.0.0
  using rmfgen-2.2.1, arfgen-1.92
in total: 3.2 Ms (!), time span: 15.9 years
Models:
1E 0102:
IACHEC model with only 1 free parameter:
  global normalization
+ gain fit (offset)
RX J1856:
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 e-19 cm-2
kT == 62.4 eV
norm == 1.58 e5
+ gain fit (offset)
Modelling temporal changes: data and models used

## Slide 27
average reduced χ2 = 10.409
Residuals obtained with xmmsas RMF
spectral models:
IACHEC model
with only 1 free parameter:
global normalization
+ gain fit (offset)
1E 0102
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 10-19 cm-2
kT == 62.4 eV
norm == 1.58 105
+ gain fit (offset)
RX J1856

## Slide 28
average reduced χ2 = 1.310
Residuals obtained with parameterized RMF
spectral models:
IACHEC model
with only 1 free parameter:
global normalization
+ gain fit (offset)
1E 0102
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 10-19 cm-2
kT == 62.4 eV
norm == 1.58 105
+ gain fit (offset)
RX J1856

## Slide 29
average reduced χ2 = 1.275
Residuals obtained with parameterized RMF
spectral models:
IACHEC model
with only 1 free parameter:
global normalization
+ gain fit (offset)
1E 0102
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 10-19 cm-2
kT == 62.4 eV
norm == 1.58 105
+ gain fit (offset)
RX J1856

## Slide 30
no obvious filter dependence
no obvious long-term trend
no obvious positional dependence
1E 0102
RXJ1856
1E 0102: no renormalization between individual filters necessary
RX J1856:
no renormalization between individual positions necessary (vignetting correction ok )
RX J1856:
no need for a second component,
parameters identical to that derived from Chandra
1E 0102:
IACHEC model works well
Residuals obtained with parameterized RMF
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 10-19 cm-2
kT == 62.4 eV
norm == 1.58 105
+ gain fit (offset)
RX J1856
spectral models:
IACHEC model
with only 1 free parameter:
global normalization
+ gain fit (offset)
1E 0102
average reduced χ2 = 1.275

## Slide 31
1E 0102: Fit quality over position and time
 no obvious dependence on position or time
SW field of view

## Slide 32
RX J1856: Fit quality over position and time
 no obvious dependence on position, no obvious long-term trend

## Slide 33
Previous spectral studies of RX J1856

## Slide 34
Chandra LETG
Chandra LETG
Sartore et al. 2012, Fig. 3
Previous spectral studies of RX J1856

## Slide 35
RX J1856: spectral fit results from new RMF
kT consistent with Chandra LETG
deviation in 3 observations (but no long-term trend and no positional trend)
 kT = 62.51 +/- 0.27 keV
Chandra LETG
(excluding 2,12,23)
Chandra: kT = (62.4 +/- 0.4) eV

## Slide 36
Sartore et al. 2012, Fig. 2
single BB fits (phabs * bbodyrad)
to singles within 0.15 – 1.2 „keV“
with nH fixed to 5.84×1019 cm-2,
using SAS v11.0: χν2 = 1.37
evidence for sporadic spectral changes
RX J1856: new RMF highlights sporadic spectral changes
large scatter
χν2 = 1.19

## Slide 37
2
Sartore et al. 2012, Fig. 2
common single BB fit (phabs * bbodyrad)
to singles within 0.15 – 1.2 ‚keV‘
with all parameters free, using SAS v11.0 + gain fit
 nH = (5.84 ± 0.04)×1019 cm-2
 kT = 61.30 ± 0.04 eV
RX J1856: major discrepancies to Chandra results with xmmsas RMF
 necessity to adopt significantly different parameters
and/or to introduce a second component
Sartore et al. 2012, Fig. 5
Previous spectral studies of RX J1856
TBabs * bbodyrad
with all parameters from Chandra
(no free parameter!)
nH == 7.25 10-19 cm-2
kT == 62.4 eV
norm == 1.58 105
+ gain fit (offset)

## Slide 38
1E 0102: Combined fit of 33 EPIC-pn spectra, r = 30“
E = 0.15 – 3.0 keV, extraction radius: 30 arcsec, small window mode, singles only
each spectrum fit with time dependent parameterized RMF
reduced chi2 = 1.382, chi2 = 15 482, 11 206 PHA bins, 11 201 degrees of freedom

## Slide 39
1E 0102: IACHEC model & XMM-Newton / EPIC-pn

## Slide 40
1E 0102: IACHEC model & XMM-Newton / EPIC-pn
new

## Slide 41
SAS RMF
parameterized RMF
What has changed in the RMF ?
E = 1.0 keV
rev 2000
SW
singles
channel energy [„keV“]
0.0
0.04
0.02

## Slide 42
What has changed in the RMF ?
channel energy [„keV“]
E = 1.0 keV
SW
singles
SAS RMF
parameterized RMF

## Slide 43
Temporal trend in the parameterized RMF
channel energy [„keV“]
par. RMF for rev 0
E = 1.0 keV
rev 0 - 5000
SW
singles
par. RMF for rev 5000
0.0
0.04
0.02

## Slide 44
Composition of the parameterized RMF
channel energy [„keV“]
E = 1.0 keV
SW
singles
sigma
gamma vtherm
sh_esep
sh_sig_l sh_sig_r
sh_rnorm
shlf_rnorm shlf_slope

## Slide 45
Parameterized RMF from 0.40 – 1.85 keV

## Slide 46
With the current RMF and ARF adjustments it is now possible to fit simultaneously the spectra of RXJ1856 and 1E0102 obtained with all three EPIC pn filters in all revolutions in SW mode without any renormalization between the filters, and using the unmodified Chandra LETG spectral parameters for RXJ 1856. The ARF adjustment requires only a slight increase of the oxygen thickness (with the same value for all filters).
Current restrictions:
only soft (< 2 keV) spectra used (to avoid complications with photon escape)
only SW mode spectra analysed (excellent photon statistics, negligible pile-up)
only single pixel events used (to avoid complications with split charges(
Extensions needed:
full spectral range
other readout modes: FF, eFF, LW, TI, BU
double pixel events
Current status

## Slide 47
discrepancy with Chandra LETG solved
no necessity to introduce a second black body
no obvious long-term trend
evidence for sporadic spectral changes
Spectral monitoring of RX J1856.5-3754 with XMM-Newton / EPIC-pn
Scientific by-product of the RMF parameterization:

## Slide 48
EPIC-pn RMF and ARF Improvement: Modelling temporal changes
Konrad Dennerl - Max Planck Institute for extraterrestrial Physics – Garching - Germany