## Slide 1: SPIN2016
SPIN2021 The 24th International Spin Symposium
October 18-22, 2021 at Matsue, Japan
Status of Polarized Solid Targets in European High Energy Scattering Experiments
G. Reicherz
Notes: In Europe are running three polarized solid state targets in single and double polarized scattering experiments. In Bonn at ELSA and in Mainz at MAMI are two targets located. Both are so called frozen spin targets, which are dynamically polarized and during data taking the material is cooled down to 50 mK and lower, where the spins are frozen what means the relaxation time is increased to few hundred up to several thousand hours, depending on temperature and applied magnetic field. The biggest polarized target in the world is the COMPASS target, running in the north area at CERN. This target can run in frozen spin and in continuous wave mode depending on the physical question of the scattering experiment. This talk presents the status of the three experiments with a focus on the targets.

## Slide 2: Content
Introduction
COMPASS
A2-MAMI
CB-Elsa
Summary

## Slide 3: Introduction
Internal targets operated in storage rings very thin (≤ 1015 atoms per cm2) polarized H targets densities nt  1013 − 1014 cm−2
Beam current I  50mA 31017e−s−1  Luminosities of 31030 − 31031 cm−2s−1
External targets solid as H targets with densities of 1023 cm-2 with beam currents < 100nA yielding in a luminosity of 6  1034 cm-2 s-1
or
highly compressed optical pumped 3He gas target density of 1021 cm-2 but tolerable beams currents up to 30uA

## Slide 4: Target: polarization techniques
Notes: Specifics of the different polarized target techniques. Dashed line --- : Up to now
laser driven sources using spin-exchange with K atoms are not routinely used for H-and D
target operation in particle physics experiments.

## Slide 5: Introduction COMPASS CERN
Structure of the nucleon
8 intrinsic transverse momentum dependent PDFs
Asymmetries with different angular dependences on hadron and spin azimuthal angles, Φh and Φs
SIDIS gives access to all of them
quark
polarization
nucleon polarization
Notes: taking into account the quark intrinsic transverse momentum kT ,
at leading order other 6 TMD PDFs are needed for a full description
of the nucleon structure

## Slide 6: COMPASS II
• Polarized Drell-Yan measurement TMD PDFs
• GPD measurement
Transverse imaging
• Pion and Kaon polarizability
Chiral perturbation theory
π-- beam with polarized proton target
μ+ μ- beam with liquid hydrogen target
π--, K- (μ-) beam with nucleus target
approved by CERN Research Board in 2010
With a upgraded COMPASS spectrometer
2014 Test beam Drell-Yan process with p beam and T polarized proton target
2015 Drell-Yan process with p beam and T polarized proton target
2016 DVCS / SIDIS with m beam and unpolarized proton target
2017 DVCS / SIDIS with m beam and unpolarized proton target
2018 Drell-Yan process with p beam and T polarized proton target
Notes: TMD transverse momentum distribution
GPD General Parton Distribution

## Slide 7: SIDIS – transversely polarized Deuteron Target Transversity/Sivers PDF extraction
A. Martin, F.B., V. Barone PRD91 (2015) 014034
TMD PDFs and Transversity h1(x) are flavor dependent
Flavour separation -> data on both proton and deuteron transversely polarized targets
Proton data set is factor 4 compared to deuteron (see error bars for transversity h1(x) in the plot below)
It’s logical to increase the deuteron data set (so far the only data sets available are COMPASS (6LiD) and CLAS (3He) target
A new measurement of SIDIS on transversely polarized deuteron
in 2021 and next year is planed.

## Slide 8: COMPASS setup in 2021
Similar setup to 2010, i. e. polarized target, large-angle spectrometer (LAS) tracking detectors. The list of detectors is about the same as in 2018 plus the silicon beam telescope.
Notes: Same setup like in 2015 increasing of the statistics

## Slide 9: COMPASS Polarized Target 2021
SIDIS of muons off transversely polarized 6LiD target • 2.5 T solenoid + 0.6 T dipole
• 50 mK dilution refrigerator
• 30+60+30 cm long 3 cells
• LiD as deuteron target
• DNP by microwave of 70 GHz
• 10 NMR coils
• Frozen spin mode at 50mK

## Slide 10: 3 target cells and 10 NMR coils
Kevlar tube

## Slide 11: 2021 Target material 6LiD
Preparation by irradiation with electrons
(Ee= 20 MeV, T=190K)
f = 4/8 = 0.5 (6Li: a + D)
COMPASS 2006
P+ = +56%
P- = -52%
Notes: Produced in Bochum in 2000 and radiated in Bonn at 20MeV Linac e-

## Slide 12: 2021 Target results
Polarization buil-up for coils 4 and 7 in the middle cell
50% polarization was reached
Bolometric EPR lines for different polarization values

## Slide 13: Measurement in 2022
Structure of the nucleon
SIDIS results on transversely polarized targets measured by COMPASS
h+ and h- (PID) TSA on d COMPASS
gluon Sivers, J/Ψ, Λ on p and d COMPASS
h+h- (PID) TSA on d COMPASS
d: statistically limited
one year of running with transversely polarized deuteron in the same conditions as in 2010 decreased the statistical errors
Notes: taking into account the quark intrinsic transverse momentum kT ,
at leading order other 6 TMD PDFs are needed for a full description
of the nucleon structure

## Slide 14: Status and plans for experiments with polarized target at MAMI
Parameter
1604MeV, sE=0.100MeV
max. 40mA polarized
eh=9 nm rad, ev=0.5 nm rad
~6500h/year
The Mainz Microtron MAMI

## Slide 15: A2 Tagging system and Crystal Ball – TAPS detector
Next Experiments with PT starting in 2022:
Deuteron Photodisintegration of d*(2380) ? Hexaquark
Baryon Spectroscopy on polarized protons
Spin Polarizabilities with active polarized targets

## Slide 16: Active Polarized Target
Notes: Polymethylmethacrylat (Kurzzeichen PMMA, auch Acrylglas) ist ein transparenter thermoplastischer Kunststoff.

## Slide 17: Active Polarized Target (First prototype 2016)
The active polarized proton target was in operation in our 4p detector system in 2016.

## Slide 18: Active Polarized Target (Improved Insert 2021)
Detailed analysis, calculations and comparison of concepts for target heads for better light collection
The mirror head shows a superior light collection efficiency.
Problem: Mechanical stability.
eg. mirror head target
wave length shifter concept
vs.
The detailed analysis in the framework of Maik Biroth gave a lot of new ideas for a better construction.

## Slide 19: Active Polarized Target (Improved Insert 2021)
The production process of the
active polarized target stacks has been optimized.
The machining procedure for post production
for NMR and cryogenic cooling slits was further developed.
The coupling of the electronic readout to the light guide
components is well under control and documented.
R&D for polarized active szintillator target for threshold production and Compton is continued. Analysis of first data proofs light output.
New active target insert with better light transport system realized by fibers is under construction.
Scintillating target container with Butanol as option.

## Slide 20: A2 - Publications
M. Biroth, P. Achenbach, E. Downie, and A. Thomas, “A low-noise
and fast pre-amplifier and readout system for SiPMs,” Nucl. Instrum.
Methods Phys. Res. A, vol. 787, pp. 185–188, Jul. 2015.
P. Achenbach, M. Biroth, E. Downie, and A. Thomas, “On the operation
of silicon photomultipliers at temperatures of 1–4 kelvin,” Nucl. Instrum.
Methods Phys. Res. A, vol. 824, pp. 74–75, Jul. 2016.
M. Biroth, P. Achenbach, E. Downie, and A. Thomas, “Silicon photomultiplier
properties at cryogenic temperatures,” Nucl. Instrum. Methods
Phys. Res. A, vol. 787, pp. 68–71, Jul. 2015.

## Slide 21: CBELSA/TAPS
Notes: Das Two-Arm-Photon-Spektrometer TAPS [Nov91] [Str96] ist ein elektro-magnetisches Kalorimeter, das in der derzeitigen Ausbaustufe aus bis zu 9*64 Barium-Fluorid-Kristallen(BaF2) besteht. Zusätzlich ist vor jedem BaF2-Kristall ein Plastikszintillator angebracht, der als Veto-System für geladene Reaktionsprodukte fungiert. Das Detektorsystem wurde 1987 von der euro-päischen TAPS-Kollaboration 1 geplant und in den daraufolgenden Jahren aufgebaut und genutzt.

## Slide 22: Baryon Spectroscopy
Aim: Better understanding of QCD and the structure of hadrons:
How does QCD give rise to hadrons?
Which hadrons – bound states of QCD – do exist?
-> Baryon spectroscopy
Fully relativistic quark model
U. Löring, B. Metsch, H. Petry, Eur. Phys. J. A10 (2001) 395
Quark models:
Many more resonance expected than observed
Certain configurations completely missing:
  Wrong degrees of freedom in quark model?
  Experimentally not found yet?

## Slide 23: CBELSA/TAPS – Polarized Target
Work in 2017
I Merging the Dubna/Mainz and Bonn Systems.
Tmin < 30mK
 p   N
two periods with Butanol
and one with D-Butanol
Frozen spin with a holding field 0.6T
Generated by very thin magnet mount on inner warming shield 
Dubna: Y. Usov, N. Borisov, I. Gorodnov et al. Mainz: A. Thomas et al. Bochum: G. Reicherz. Bonn: S. Goertz, H. Dutz, S. Runkel et al

## Slide 24: Data taking 2021
D-Butanol October 2018
H-Butanol June 2021
H-Butanol May 2018
Next run at CB-ELSA will start on Oct 27th with D-Butanol!

## Slide 25: CryPTA: Cryogenic Polarized Target Applications
Notes: STRONG-2020 “The strong interaction at the frontier of knowledge: fundamental research and applications” has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 824093.
Production of polarized nucleon targets (at the prototype level) using solid state materials combined with superconducting high-field magnets and the Dynamic Nuclear Polarization method.

## Slide 26: Summary
COMPASS runs the largest polarized solid target in the world to investigate the structure of the nuclei.
In Mainz and Bonn are running frozen spin targets in double polarized scattering experiments to determine the baryon spectroscopy The recent activities leads to 4 continues mode target concept for real photon
double polarization experiments at ELSA and MAMI
and the development of a polarized active szintillator target for threshold production
and Compton is continued.