## Slide 1: Positron source and target in KEK
2023/11/7
Y. Enomoto

## Slide 2: KEK and positron
From TRISTAN to ILC
  KEK LINAC has keep providing positron beam to e+e- collider experiment since 1980s.
  Positron source for SuperKEKB is world’s most intense positron source in operation.
  We play an important role to develop future positron source for ILC.
TRISTAN
KEKB
SuperKEKB

## Slide 3: Comparison of high-power targets in Japan
Chart: 
 | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
 | 2.5 | 55.2 | 996.9 | 520 | 730 | 87.6 | 64
Chart: 
 | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
 | 2.5 | 55.2 | 996.9 | 520 | 730 | 87.6 | 64
 | e+ | e+ | μ | n | Neutrinos | Hadrons | RIBF
Institute | KEK (SuperKEKB) | ILC (e-driven) | J-PARC | J-PARC | J-PARC | J-PARC | RIKEN
Primary particle | e- | e- | p | p | p | p | C~U
Target material | W | W | C | Hg | C | Au | Be, W
Energy [GeV] | 3 | 3 | 3.5 | 3 | 30 | 30 | 0.345/u
Charge/pulse [nC] | 10 ✕ 2 | 3.7 ✕ 66 | 13300 | 13300 | 52900 | 16470 | CW
Repetition [Hz] | 50 | 100 / 300 | 25 | 25 | 0.47 | 0.19 | CW (1puA)
Beam Power [kW] | 3 | 74 | 1000 | 1000 | 750 | 95 | 82
Beam size σx ✕ σy [mm] | 0.5 ✕ 0.5 | 2 ✕ 2 | 3.5 ✕ 3.5 | 37 ✕ 17 | 4.2 ✕ 4.2 | 2.5 ✕ 1.0 | 0.42 ✕ 0.42
Thickness [mm] | 14 | 16 | 20 | 2000 | 909 | 66 (6 ✕ 11) | ~mm
Deposited power [kW] | 0.5 | 18.8 | 3.1 | 480 | 20 | 7.4 | 18
PEDD [J/g] | 27.5 | 33.6 | 20 | 1.1 | 190 | Slow extraction | CW
Cooling | Water | Water | Radiation | Water | He | Water | Water
structure | Fixed | Rotating | Rotating | Liquid | Fixed | Fixed | Rotating
Power (kW)
■■ beam power
■ deposited power
ILC
RIBF
n
H
μ
ν
ILC
RIBF
n
H
μ
ν
SKEKB
SKEKB

## Slide 4: Particle sources and positron source
Neutron source
Muon source
Neutrino source
Electron source
Ion source
Primary particle source
secondary particle source
Positron source is installed in the middle of accelerator
Collection and acceleration of secondary particles
need high power primary beam for full test
  Usually impossible before construction
Positron source source
Accelerator
High quality beam for acceleration
Stand alone test is possible
No radiational, thermal requirement
Low beam quality is acceptable
Need high power primary beam
Severe radiational, thermal requirement

## Slide 5: Positron source for SuperKEKB
Originally developed by SLAC
Almost all the other positron sources follows this design
Surrounded by solenoid → limited space
Need UHV （<10-6 Pa）
FC = pulsed coil (20 kV, 12 kA) installed close to target (2mm)

## Slide 6: SuperKEKB target
W（Φ4 ✕ L14）、HIP to Cu block for cooling
Hole for electron
Beam power 3 kW (3 GeV ✕ 10 nC ✕ 2 bunch ✕ 50 Hz)
Deposition ~ 0.7 kW
PEDD : 27.5 J/g

## Slide 7: temperature
Pulsed heating every 20 ms by beam
Amplitude ~ 200℃
20 ms
Y. Morikawa

## Slide 8: stress
Caused by difference of thermal expansion coefficient and edge geometry (580MPa)
Beam heat peak
(140 MPa)
Caused by difference of thermal expansion coefficient and edge geometry (610MPa)
Beam heat peak
(30 MPa)
Thermal stress by pulsed beam
High at Cu-W contact surface
Care must be taken to fatigue
50 Hz = 4 ✕ 106 /day
Y. Morikawa

## Slide 9: Withstanding heat load
~3700 K
(456 J/g)
~2160 K
(250 J/g)*
~1500 K
(161 J/g)
~870 K
(77 J/g)
Melting point
Single pulse
destruction
embrittlement by
recrystallization
fatigue
Value in （） varies design of target.
Here target of SuperKEKB is assumed for reference.
*thermal stress reach 1 GPa
Melting point
  Unavoidable Limit
Single pulse destruction
  Thermal stress exceed material yield strength
  Short pulse beam → instantaneous temperature rise
Embrittlement by recrystallization
  W-Re alloy shows better value
    Difficult to obtain large size
  Advanced W alloys are one of research field
    JPS Conf. Proc. 28, 031002 (2020)
Fatigue
  limit by repetitive thermal load by pulsed beam

## Slide 10: From SuperKEKB to ILC
Based on SuperKEKB
Big jump from SuperKEKB
3 x SLC in beam power (74 kW)
4 x SuperKEKB in capture efficiency
Chart: e- beam power (kW)
| 8.9999999999999993E-3 | 1.52E-2 | 4.2999999999999997E-2 | 0.125 | 4 | 0.91200000000000003 | 1 | 3.5 | 4 | 13.32 | 27 | 56.32 | 62.9 | 73.260000000000005
Ne+/Ne-/GeV | 0.073 | 0.063 | 0.05 | 0.014 | 0.0375 | 0.013 | 0.03 | 0.114 | 0.025 | 0.11667 | 0.036 | 0.28 | 0 | 0.43
●past
▲present
◆future
ILC e-driven
High power
High efficiency
SLC
SuperKEKB
FCCee
ILC undulator
CLIC
CEPC
KEKB
BEPC
DAFNE
VEPP-5

## Slide 11: Latest 3D model for ILC positron source
Rotating target
RF cavity
solenoid
Flux concentrator

## Slide 12: Rotating target in Japan
 | e+ | μ | Hadrons | RIBF
Institute | ILC (e-driven) | J-PARC | J-PARC | RIKEN
Primary particle | e- | p | p | C~U
Target material | W | C | Au or W | Be, W
Repetition [Hz] | 100 / 300 | 25 | 0.19 | CW (1puA)
Beam Power [kW] | 74 | 1000 | 150 | 82 (design)
Deposited power [kW] | 18.8 | 3.1 | 11 | 18 (design)
PEDD [J/g] | 33.6 | 20 | Slow extraction | CW
status | Prototype | In operation | Prototype | In operation
Cooling | Water | Radiation | He | Water
Thanks to
J-PARC Muon: Matoba, Makimura
J-PARC hadron: Sawada, Takahashi, Watanabe
RIKEN RIBF: Yoshida, Yanagisawa

## Slide 13: To do
Water cooled UHV compatible rotating mechanism
Robust W-Cu connection
RF cavity after the target
  ~a few 10 kW heat load from shower
Flux concentrator compatible with rotating target
Exchange mechanism of highly activated materials in accelerator tunnel
  Not in special target area
  Deep underground (~100 m) and limited space
Grant from MEXT
FY2023 ~ FY2027
Development started 2022/Q4

## Slide 14: 5 years-plan
FY |  | 2022 |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  | 
year |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 
Quarter |  | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1
Test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
High power test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
W-Cu connection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Target unit | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3rd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC base | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
magnet | Solenoid + ST |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chamber, vacuum, support |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Acc. Structure | Dummy |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RF power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design
Manufacuring
test

## Slide 15: Test bench for ILC positron source

## Slide 16: Summary
Say hello to the high-power target community from positron group
Different requirement and limitation from proton machine
  Most of the technologies are still useful for us
Requirements of the ILC, linear collider, are very high
We started development for ILC recently
  Details about rotating target → next talk

## Slide 18: Bunch structure
Create positron for 66 ms
Store them in the DR for 199.3 ms
Extract them to main linac for 0.7 ms
20 pulse / train
66 bunch / pulse
1320 bunch / train
Repetition 5 Hz
FC must keep field variation below the requirement to keep bunch-by-bunch charge variation
Minimum current pulse width is about 500 ns
M. Kuriki, OHO seminar 2021
…….
3.3 ms✕20 = 66 ms
66
train
pulse