## Slide 1
LBNF Hadron Absorber – Design Status & Assembly Planning
Jonathan Williams – FNAL Target Systems Department
High Power Targetry Workshop
7 November 2023

## Slide 2: Outline
LBNF Overview
System Requirements
Design Overview
Assembly & Installation Planning

## Slide 3: LBNF Overview

## Slide 4: Long-Baseline Neutrino Facility
Make the neutrino beam for DUNE
Protons on a graphite target > focus pions > decay to neutrinos
What happens to the protons? Everything else?

## Slide 5: LBNF-30: Absorber Complex
Beamline
Decay Pipe
Hadron Absorber
Muon Monitors
& Shielding
Muon Kern
Access Hatch
Service Building

## Slide 6: Absorber Requirements
Intercept primary proton beam
  2.4 MW @ 120 GeV: 1.2s cycle time, 1.5E+14 protons per pulse
  2 full-power accident pulses, assuming no hit on target or baffle
Beam permit interlock
  Active detection, limit accident pulses to 2
Serviceability & Accident Resiliency
  30-year design life, allow for future upgrades/replacements in core (plus morgue space)
Structural Integrity
  Interface with decay pipe
Radiological Safety
  Interventions and Operations - ALARA

## Slide 7: Design Overview

## Slide 8: Concrete Blocks
48x “G”-blocks, 24ft x 3ft x 1.5ft (7.32 m x 0.91m x 0.46m)
  Includes 10x heavy mix concrete at top upstream end (extra boron)
“T”-shaped blocks for downstream face
  Provide labyrinthing
G-Blocks make an air seal over pile
  Air supply for cooling
  Isolate absorber/morgue air volume from Hall
  Need to redo caulking after interventions

## Slide 9: Bunker & RAW Pan
Bunker
  Morgue: 4 core modules, 2 hadron monitors (HADES)
  Air inlet & exhaust
  Water supply manifold
Stainless steel pan (1/4” thick) to catch water leaks from core
  Leveling during assembly is crucial
  Embeds in wall to attach sides of pan

## Slide 10: Outer Steel Shielding
1.2 million pounds Continuous-Cast Salvage Steel (CCSS)
130 Duratek S2 Shield Blocks (Blue Blocks), 20,000 lbs each (2.6M total)
  Blue Blocks are air-cooled

## Slide 11: Core Modules & Supports
Steel T-Block (air-cooled)
  Absorber based on NuMI target shield pile
Aluminum core blocks (water-cooled)
  Staggering along beam direction – wide/narrow blocks
Spoiler
Mask
Al Core
Steel Core
HADES (left)
Pre-Spoiler Air Box (right)
Module Supports

## Slide 12: Core Modules & Supports
Spacer plates between supports maintain air gap
  Leveling screws on modules
Bring in modules after chase is complete
  Take time to align/level each module to ensure spacing

## Slide 13: Core Blocks

## Slide 14: Core Blocks
Prototype Core Block – Engineer for scale

## Slide 15: Core and Shielding – Active Cooling
1310 gpm water @ 80 F (27 C), 5-7 ft/s in passages, 80 gpm core, 40 gpm mask (229 kW @ 2.4 MW)
25,000 CFM air, 32” water column, 5 mm gap, 15m/s velocity (244 kW @ 2.4 MW)
Water manifold has leftover blank ports

## Slide 16: On-Axis View

## Slide 17: Assembly & Installation Planning

## Slide 18: Ship in a Bottle
Open-air access hatch
  All components lowered via external crane
Installation bottleneck
  Limited space downstairs for storage
    Just-in-time delivery
    Hard to install components in parallel
Receiving Stand

## Slide 19: Core Module Assembly
Core module water loops are gundrilled, with welded-on supply lines
  Assemble vertically: 1G position for aluminum welds
Store vertically, then transport to Absorber Hall
Assembly Stand
Storage Stand (20x G-Blocks, reuse for Absorber)
Down-Shaft Receiving Stand

## Slide 20: Water Line Welding
Need rigorous qualification of aluminum welds
  Can’t radiograph core module/elbow welds
  Planning more weld tests with destructive inspections

## Slide 21: Module Transport
Rotating strongback/transport cradle
Rotation fixture at hatch and storage location, transport flat by trailer
Rotation Stand & Transport Frame

## Slide 22: Outer Shielding Installation
Upstream and downstream walls require welding
  HADES supported by upstream wall
Examining “loose” stacking of CCSS slabs on sides
  Restrained by core supports, blue blocks, and the bunker wall
Assembly model
  Catalogue parts by size - Bunker walls are hard limit, everything has to fit
    Blue block dimensions are (+.25”/-.75”)
    CCSS slabs will likely have camber
  Filler plates to close off any gaps from undersize parts

## Slide 23: Installation Overview
*Plans have changed!

## Slide 24: Design & Documentation – What’s Left?
Final Design Review scheduled for February/March
  Final design of core modules recently completed
  Installation sequence – step-by-step drawings (layer by layer)
    Groundwork for assembly model with serialized components
  Bunker design is set in stone concrete
    Procurement process has begun for construction contract

## Slide 25: Questions?

## Slide 26: Backup

## Slide 27: Radiation Modeling
FNAL MARS group has been extensively modeling the Absorber
  Recent changes to air supply duct, modeling residual dose in air
Scale is mSv/hr
Beam on (2.4 MW) prompt dose
Beam off (110 d irr., 4 hr cooling) contact residual dose
  DUNE-DocDB-17021-v5

## Slide 28: Heat Deposition
DUNE-DocDB-17064, S. Striganov
*Data for 2.4 MW operation
mW/cm3

## Slide 29: Challenges & Some Solutions
Future-proof active cooling systems - design for 2.4 MW
    Maintain all temperatures within material limits – 100 C fatigue limit for 6061-T6 core blocks, 230 F for anti-corrosion paint on steel
Absorb secondary particles and radiation
  Steel backstop, muon kern downstream
How to detect bad beam quickly?
  224 thermocouples (in beam) in core module 2
  Scaled-up NuMI system (4 TCs)
  dT/pulse limit: <1 degree normal, 16-90 deg for accidents
  Water line could be hit by beam: modeling work
Thermocouple Core Module

## Slide 30: Challenges & Some Solutions
How to minimize worker dose?
  Remote crane operations, minimize touch labor on top of absorber
  (water line connections & wiring only)
Graphics: V. Sidorov
Conceptual stacking layout for HADES access

## Slide 31: Challenges & Some Solutions
Thermal Expansion of Decay Pipe
  200m length – lots of steel and concrete to expand with beam heating
  6” (~15 cm) expansion allowance
  Low clearance between downstream decay pipe window & HADES
Expansion coefficient for poured concrete ~ 10 µm/m*C °
  200m, 10 C° = 1 cm linear expansion
6” gap
LBNF-30
Foundation
Decay Pipe
Concrete Shielding

## Slide 32: NuMI Target Shield Pile
NuMI Target Shield Pile Installation
3-high on-edge Blue Block stack
  LBNF Absorber has 5-high stacks
  Blue blocks modeled oversize, shimmed to fit and level
NuMI Target Shield Pile Mockup

## Slide 33: HADES Retractive System