## Slide 1
Dan Wilcox
Rutherford Appleton Laboratory, UK
For UK team in collaboration with Fermilab LBNF Targetry Project Team, UK Universities, and Culham MRF
8th High Power Targetry Workshop
November 7th 2023
LBNF Target Design

## Slide 2: Overview
UK project overview
Target challenges
Prototype target design
  Engineering analysis
  Prototype manufacturing
  Irradiated material studies
Future plans and deliverables

## Slide 3: LBNF and DUNE
Neutrinos
Out
Accelerated Protons In
Physics highlights:
World’s most intense neutrino beam
Longest distance to detector
May indicate why the Universe is made of matter
Pions decay to muons and neutrinos
Target absorbs protons, produces pions
See talk by Patrick Hurh on Thursday 9th

## Slide 4: Scope of UK Targetry Contribution
1x Target Exchange System:
1x Instrumented Baffle:
Targets and Connecting Pipework:
1x Prototype Target
1x Production Target
Various Helium Plant Components inc. Blower and Coolers:
Protons

## Slide 5: UK Project Timeline

## Slide 6: Comparison with T2K
Parameter | LBNF Design (1 Year Design Life) | T2K Experience (Target 2 History)
Beam Power (MW) | 1.2 | 0.51
Proton Energy (GeV) | 120 | 30
Beam Current (μA) | 10 | 17
Beam Sigma (mm) | 2.7 | 4
Radiation Damage Severity (p/cm^2) | 2.5E+21 | 3.1E+21
Thermal Shock Severity (p/cm^2/pulse) | 1.7E+14 | 2.6E+14
Higher beam power and smaller beam spot, but lower current = lower proton fluence and thermal shock than T2K
Longer target will require optimised design of cantilever support
c/o Patrick Hurh (Fermilab)
T2K
LBNF
To scale. Core length = 0.9m T2K, 1.5m LBNF

## Slide 7: Target Engineering Challenges
Protons
Proton beam causes very high heat deposition and radiation damage (several DPA/yr along beam centreline)
1.5m long cantilever – must not touch the inside of the horn
Vessel wall must be thin to prevent pion reabsorption, but strong to contain pressure and support cantilever
Support structure must align the target very accurately relative to the horn and proton beam
Target core temperature jumps by 140°C in 10ms, once every 1.2s – thermal shock and fatigue
Vibrations transmitted from horn to target mount
Materials must be strong and perform well at high temperature:
Nuclear-grade graphite core
Titanium alloy outer container

## Slide 8: Physics Optimisation of Engineering Features
Small effect of varying support fins
Larger effect of increasing target length
Very large effect of changing vessel thickness
Prototype Target
c/o John Back (Warwick University)
Vessel Wall Thickness
Total
Target Length
Size of Support Fins

## Slide 9
 | Grade 2 (CP Ti) | Grade 9 (Ti-3Al-2.5V) | Grade 5 (Ti-6Al-4V) | Ti 15-3 (Ti-15V-3Cr-3Al-3Sn)
Prior Operating Experience | None | None | Used in T2K target | Non-pressure use at T2K
Pressure Code Approval | Listed in ASME | Code route exists | Code route exists | No previous code use
Structural Safety Factor | Lowest | Higher than grade 2 | Higher than grade 9 | Even higher than grade 5
Radiation Damage Tolerance | No data available | Better than grade 5? | Good data and T2K use | Looks best, but needs R+D
Ease of Manufacture | Successful prototype | Difficult to machine | Successful prototype | Welding not yet tested
Ease of Procurement | Widely available | Less widely available | Widely available | Limited availability
Prototype Target Titanium Grade Selection
Note that it must also be possible to weld the selected vessel and window grades together
Ti 15-3 window prototype c/o
T. Ishida

## Slide 10: Detailed Target Analysis
Fluid:
Thermal:
Structural:
Fatigue:
Geometry:
Mesh:
Radiation Dose:
Stress Categorisation:
Pressure Code Approval
(FESHM and ASME BPVC)

## Slide 11: ASME BPVC Required Analyses
Plastic Collapse
  Stress categorisation and/or plasticity analysis
Buckling analysis
Fatigue
First buckling mode with no internal support structures
Goodman equivalent stress amplitude in vessel and windows

## Slide 12: Radiation Dose with Nominal Beam, 1.2MW
DPA is highest in the windows (2.5/yr) and target (0.5/yr)
Peak DPA in any other component is 0.26/yr, in the flow divider tube
Some titanium irradiation data available for up to 0.24 DPA

## Slide 13: Irradiated Titanium Data Summary – Grades 5 and 23
“Fatigue Performance of Proton Irradiated Ti6Al4V Alloy”, Sujit Bidhar, 6th RaDIATE Collaboration Meeting, Dec 10, 2019
Macro-scale Fatigue
Gr5/23
Dose at neck region
0.06~0.24 DPA
Irradiation temp
50C~125C
R=0.2-0.28
Meso-scale Fatigue
Gr23 A&STA, Gr2, 15-3Ti
Meso-scale S-N Curve of unirradiated Ti-6Al-4V
V. Kuksenko, RaDIATE2017
Tensile Testing
Gr5/23, Gr9
“Tensile behavior of dual-phase titanium alloys under high-intensity proton beam exposure…”, T. Ishida et al., Journal of Nuclear Materials, 2020

## Slide 14: Radiation and Fatigue in Titanium
Windows have the highest radiation damage and fatigue of any Titanium component
Upstream Window
tmin = 0.3mm
Dose = 2.5dpa/yr
Tsteady = 115°C
Tmax = 150°C peak
ΔT = 70°C/pulse
ΔσEq = 21MPa/pulse
Downstream Window
tmin = 0.4mm
Dose = 0.7dpa/yr
Tsteady = 150°C
Tmax = 175°C peak
ΔT = 55°C/pulse
ΔσEq = 6MPa/pulse
Extrapolated Endurance Limit for >1E9 Cycles (MPa) | SE (MPa)
Titanium Grade 5 | 360
Derated for 150°C | 315
Derated for 150°C and 0.24DPA | 240
Expected number of beam pulse cycles = 1.5E7 per year

## Slide 15: Radiation and Fatigue in Graphite
First two target segments have highest radiation damage and fatigue of any Graphite component
 | IG-43 Graphite
UTS at room temp (MPa) | 37
Estimated endurance limit (MPa) | 18.5
Equivalent stress amp. (MPa) | 0.95

## Slide 16: Horn-Induced Vibrations
Identified risk of vibrations from the magnetic horn being transmitted to the target
  Physical testing not possible for several years; must rely on simulation expertise
Benchmark against T2K Horn measurements:
Combined simulation of horn and target:
Axial vibrations transmitted
from horn to target mount
(Peak applied acceleration ≈20g)
*Deformation not to scale
c/o T. Sekiguchi (KEK)

## Slide 17
Alternative geometries developed and tested in simulation
  Proposed solution works well over a broad frequency range, and is easy to modify if future testing does find issues
Horn-Induced Vibrations

## Slide 18
Feature Prototyping Highlights

## Slide 19
Quotes received
Production challenges identified at PDR

## Slide 20: Ongoing Prototyping Efforts
Full length target core segment prototype completed:
Target core mounting design development:

## Slide 21: Target Weldment Order of Fabrication
Weld 3
Weld 1
Weld 4
Weld 2
Weld 5
Weld 6
Weld 11
Weld 10
Weld 7
Weld 9
Weld 8
TD-1268-643
Bafflette can
TD-1268-211
cross-flow
TD-1268-622
exhaust mf.
TD-1268-414
funnel
TD-1268-415
Cone
TD-1268-680
Vessel section A
TD-1268-702
DS window
TD-1268-586
DS flow guide
TD-1268-658-XX
US window
TD-1268-657
USW housing
TD-1268-681
Vessel section B
TD-1268-682
Vessel section C

## Slide 22: Irradiated Material Collaborations
Titanium
Graphite
Highest dose to beam windows:
Titanium irradiation at BLIP:
Meso-fatigue specimens have been shipped to Culham MRF:
Fatigue test in hot cell, using a method developed at Oxford University*:
Cracked graphite targets seen at NuMI-MINOS and other facilities:
- Active sample on its way to Bristol University
- Neutron diffraction experiment at ISIS (ENGIN-X) approved
Future Ti irradiations also planned at Birmingham University
*See poster by Richard Cowan

## Slide 23: Conclusions
Phase 1 (Design) complete and closed out. Phase 2 (Construction) fully funded
Design and analysis of prototype target completed, initial manufacturing now underway
Focus will now be on:
  Completing construction of working prototype target
  Irradiated material studies to inform design of future targets
  Refine design, then construct 1st production target

## Slide 25
Backup Slides

## Slide 26: Main Baffle Design
Graphite core segment stack
Prototype
core
segments

## Slide 27: Baffle Protection Against Off-Axis Beams
FLUKA simulations by John Back of Warwick University
  Radial offset of 17.25mm to directly hit target flowguide
A direct hit through the main baffle produces less heating than the shower from the target during normal operation
Off-Axis, Impinging on Flowguide
Normal Operation
Case | Peak heat in flowguide | Delta T per Pulse
 | W/m^3 | C
Normal Operation | 5.54E+07 | 26.8
Off-Axis | 1.06E+07 | 5.1

## Slide 28: Target Exchange System (TXS)
Rail system for remote exchange of targets in hot cell
Based on a similar system successfully deployed at T2K

## Slide 29: TXS Testing at RAL
Very accurate alignment required to avoid damage to target or horn
Mock-up to test procedures and alignment mechanism built at RAL
Compliance mechanism
Dummy target mass
“Green plate”
“Red plate”
Insertion rail

## Slide 30: Helium Plant Deliverables
v
  1x Positive Displacement Blower
  1x back-up blower (Working Allowance scope opportunity)
  1x Target RAW Cooler
  1x Compressor Pre-cooler
  1x Compressor After-cooler
  1x remote operable gas purity monitoring system
x 3
x 1
x 1(/2)
e.g. Kelvion: Welded Plate and Frame Heat exchanger
e.g. Hiden: HPR-20 benchtop mass spectrometer
Custom machine: identified two potential European Suppliers