## Slide 1: Overview of the design status of IFMIF-DONES Lithium Target System J. Maestre on behalf of WPENS

## Slide 2: Outline
Introduction to IFMIF-DONES
Validations and prototyping
Target System
Summary
Overview to Lithium systems

## Slide 3: Introduction
Neutron spectrum up to 55 MeV energy
High Flux Test Module:
20 dpa/fpy in 100 cm3 of material
IFMIF-DONES is and accelerator-based fusion-like neutron source for
the qualification of the materials oriented to DEMO
DEMO: Fusion reactor
Being designed to operate continuously providing electricity to the grid (~2-4 GW), showing commercial nuclear fusion is technically feasible. Q>10, 2050
~20 dpa/year

## Slide 4: Lithium Systems: overview
beam
Top level requirement: To generate a stable liquid lithium target for enabling D-Li stripping reaction and producing an adequate neutron flux to properly irradiate the test modules downstream.
Target System: To provide a continuous Li jet whose interaction with D+ beam generates the Neutron flux.
Heat Removal Loop: To remove the energy deposition on the Lithium.
Impurity Control System: To localize and control the impurities in the Lithium.
Accelerator System
Test System
Lithium System
Main parameters:
Li inventory ~14 m3
Li flow rate ~100 l/s
Li working temperature (cold side) 300 °C
Deposited power: 5 - 10 MW
Test Cell
Li Target
Li Systems

## Slide 5: Target System: description
Fig. Velocity field distribution in the nozzle and BP
Nominal liquid Lithium jet speed of 15 m/s at the exit of the nozzle
Curvature of BP for avoiding Li boiling
25 mm thin Li jet and slim Back Plate to reduce neutron re-absorption (1.8 mm)
Hydrodynamic optimization preventing cavitation/boiling
To optimize the production of an intense enough neutron flux to irradiate the test module.
To remove beam energy deposition (5MW-10 MW)
Two type of beams 200 x 50 mm2 and 100 x 50 mm2
Main requirements
Design
Many supporting analysis
Inlet nozzle
10E-4 mbar
50 mm
200 mm
Fig. Distribution of the energy deposition in the Li jet as result of beam-Li interaction
Thermo-hydro-mechanics (most recent studies):
Updated thermo-mechanical and hydrodynamic analyse of the Target System (E2QEFZ9). (2023.Sep)
Update of seismic analysis of Target System (2QAPVV) (2023.Jun)
Detailed design of TCE penetrations and piping connections in the LS (2PMGUU) (2022) and other anchoring TSY-HFTM (2PE8MK)
Fatigue evaluation induced by fast Beam Transient (2020)
Final numerical analysis of Li jet, BP discharge line and QT for beam on operation conditions (2NTGD9) (2020.Oct).
Consequences on Beam shift in transversal direction (2NXPR9). (2023.Mar)
Thermal induce pressure waves due to beam trips (2NKLFE) (2021.May)
Consequences of reduced jet thickness during operation condition. (2NHYG5) (2019.Feb)
Etc.
Through wall beam duct

## Slide 6: Target System: analysis
High density power deposition ~85 kW/cm3
Deuterium Bragg - Peak at 20 mm (25±1 mm thickness)
Design for two different Deuterium beam: 200 x 50 mm2 and 100 x 50 mm2
High temperature in the bulk lithium (~425ºC), while the average temperature is 318 ºC
QT homogenizes the temperature and quenches the flowing lithium before being reinjected to the Li loop
P= 10E-4 mbar
Fig. Temp distribution in the Li jet and Quench Tank during beam on
Fig. Beam energy deposition on the lithium jet
Analysis under nominal conditions
Courtesy of S. Gordeev, A. Serikov, Q. Yuefeng (KIT, Germany)

## Slide 7: Target System: analysis
Pressure distribution along the back Plate
P [Pa]
Cte curvature
Variable curvature
Chart: Vapour pressure of Lithium
- VLi 20 m/s
- VLi 15 m/s
- VLi 10 m/s
Margin in temp.
Margin in pressure
- VLi 20 m/s
Suitable design of the Back plate to prevent boiling at the free surface and inside Li jet.
Analysis of different Back Plate shapes and flow velocities. Variable curvature provide a smooth pressure variation along the BP.
BEAM
P [Pa]
Y
- VLi 20 m/s
Variable curvature
P= 10E-4 mbar
Pressure distribution in the Li jet
Analysis under nominal conditions
Lithium jet is exposed to the Accelerator vacuum 10-2 Pa
Risk of Lithium boiling.
By f. S. Nitti (ENEA, Italy)
Beam

## Slide 8: Target System: analysis
Li jet thickness reduction due to a degradation/defect of the Li inlet Nozzle
Temperature difference of 9ªC (1mm) and 16ºC (2mm) on the Back plate side.
No damage to the BP
Note that the simulation was made for a nominal temp of 250ºC
Simulations detect no occurrence of cavitation in the zone of low pressure after the beam-off.
Maximum pressure is reached for a sudden beam-on with a span of 30 us, this being 0.3 MPa.
No damage BP, including Fatigue analysis.
Beam off
Beam on
Beam on
Beam on
According to experts and previous operational experience (LIPAc), there can appear beam trips (beam off-on) O(ms).
Parametric analysis of trips
Analysis under off-nominal conditions
Inlet nozzle
Beam on
By S. Gordeev (KIT, Germany)
Li jet
Li jet

## Slide 9: Target System: analysis
Working temp 300ºC + 90 (DBTT)
~8-9 months working at full power
EUROFER (Ferritic/martensitic steels ) exhibits a shift on its behaviour from ductile to brittle for a given range of temperature, called DBTT. No irradiated one is about ~ -90 °C, so it is not an issue for normal applications.
When the material is irradiated with high energy neutrons, the DBTT increases and, at high doses, it can eventually reach the operating temperature
Rough estimation of lifetime of the Back Plate based on DBTT as F(irradiation time)
The strategy is to periodically replace partially or completely the Target during the yearly long maintenance
Integral concept of Target
Removable BP concept
Integral design concept is currently considered as baseline design whereas the removable version is validated.
Analysis of lifetime
welded BP
Mechanism to remove BP. It relays on energized gaskets (Helicoflex)
By D. Bernardi (ENEA, Italy)

## Slide 10: Target System: replacement
Replacement strategy and features
Ball joints, slides
Excentres
Small gearboxes
Spindle drives, slides
Small gearboxes, spindle/nut, slidings (ceramic/ceramic or steel/ceramic)
QDS
TX
TX
TY
TZ
TZ
TX
TY
FDS
Fiducials
Gearboxes, spindle/nut, flexible shafts (remain in the TC)
Guided Fast disconnection system
There are 4 connections points: Through wall beam ducts; Inlet pipe; Outlet channel
Target supported by the Target Support Structured attached to the floor of the Test Cell
Linked with the HFTM
Remote handling compatible

## Slide 11: Validations and prototyping (IFMIF-EVEDA)
Engineering validation for lithium target facility of the IFMIF under IFMIF/EVEDA project. Nuclear Materials and Energy, Vol 9, pag. 278-285 (2016)
Fig. Prototype of the Target
Fig. free jet taken with 2 s and 10 µs exposure time
Facility for corrosion/erosion test under flowing lithium N-trap: Control of N impurities
A. Aiello et al. Lifus (lithium for fusion) 6 loop design and construction. Fusion Engineering and Design Volume 88, Issues 6–8, October 2013, Pages 769-773
Fig. ELTL facility in Japan
Fig. Lifus-6
Lithium Test Loop (ELTL) at Oarai (Japan) during IFMIF/EVEDA
Lithium loop at real scale 1:1 for loop high and 1:2.6 for target width with respect to DONES.
Long time operation (>3800 h)
Fluid-Dynamic stability of the Li jet (1300 h). Suitable flatness of the free surface (non uniformity < 0.28 mm)
Li jet ranging from 10 - 20 m/s
Validations
  Lifus-6

## Slide 12: Validations and prototyping (WPENS)
Prototype of QDS/FDS
Target Mock-up
Li diagnostics
Manufacturing of prototype for connection and disconnection mechanism (QDS) by remote control in IFMIF-DONES project
Experimental campaign of IVVS sensor for the Li target 2022 (EFDA_D_2PGCLA v1.1)
IVVS
Results of Target Pre-heating Test (EFDA_D_2NHGLF v1.0)
Heating jacket
Back Plate
Manufacturing of prototype for connection of the fast disconnection system (FDS) of the Li inlet pipe
Analysis of the RH procedure of the TSY

## Slide 13: Summary
Intense design & validation work was already carried out during IFMIF-EVEDA (2010), proving the successful operation and main key technologies of the Lithium system (including the construction of ELTL prototype).
This design work has been continued within EUROFUSION WPENS, reaching a higher definition level supported by many analysis, and thanks to the contribution of different Research Units (and industry).
Most of definition design activities are to be concluded soon, whereas engineering validation activities are on-going for gaining farther experience and increasing TRL before handover. Main pending validations:
  Removable concept of the Back Plate of the Target.
  Replacement strategy of the Target System and auxiliary sub-systems.
  Diagnostic.

## Slide 14: Thanks Any advice or suggestion is welcome

## Slide 15: Introduction
ITER (800 m3)
ITER under construction in Cadarache (France). To demonstrate the scientific feasibility of fusion energy (500 MW of power from fusion energy with Q>10) no connected to the grid.
DEMO (~1000-3500 m3):
Being designed to operate continuously providing electricity to the grid (~2-4 GW), showing commercial nuclear fusion is technically feasible. Q>10, 2050
JET (80 m3)
JET started its operations in 1983. It was designed to study plasma behaviour in conditions close to those required for a fusion reactor. (16MW and Q<1 still)
MAGENETIC CONFINEMENT FUSION
1-3 dpa/lifetime
~20 dpa/year
Main challenge:
Materials capable of withstanding the thermal loads and irradiation effects that may occur on the chamber walls.
See https://www.euro-fusion.org/eurofusion/roadmap/
Engineering Standards

## Slide 16: Introduction
Granada (Escúzar)

## Slide 17: Lithium Systems: overview
Accelerator System
Test System
Lithium System

## Slide 18: Target System: Description
Challenges:
Hydro-dynamic stability of the of Li
High corrosion and erosion of Lithium with structural material
High reactivity of Lithium
Target System exposed to extreme conditions: ~20 dpa/fpy; Thermo-mechanical loads
Main parameters:
Li inventory ~14 m3
Li flow rate ~100 l/s
Li working temperature (cold side) 300 °C
Deposited power: 5 – 10 MW
Target System is allocated inside Test Cell, concrete cell covered by a stainless-steel liner under a controlled environment (He or Ar)
No safety credit is provided to the Target. TC liner is considered the confinement barrier together with the penetration, closed by safety valves.
Temperature of the liner controlled by water cooling system on the outside
Beam

## Slide 19: Target System: replacement
Replacement strategy and features
RTASP2
RTASP1
RQTO
RBD1
RBD2
RIPF
TWBD flange position
RTASP1/2
RQTO
Fixed references
Target System Structure
Through wall beam duct
Quench Tank
There are 4 connections points: Through wall beam ducts; Inlet pipe; Oulet channel
Supported by the Target support structured attached to the floor of the Test Cell
Linked with the HFTM
View without the Target
By T. Dezsi