## Slide 1
A new spallation-driven, two-step target at ISAC-TRIUMF
Luca Egoriti
8th HPTW, Wako
November 10th 2023

## Slide 2
TRIUMF accelerators
Muons for
material science
500 MeV – 400 μA
H- Cyclotron
PIF
STF
T1
T2
82Sr medical production
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
TR: 13
TR: 30-1
TR: 30-2
CP: 42
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from ~2025)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL1A
ITW
ITE
ISOL
(ISAC)
BL2A
BL2C
BL4N

## Slide 3
ISOL targets for RIB production
500 MeV – 100 μA
P+ Cyclotron
Extraction electrode
HV 60 kV
Target
T=2000 °C
2 kV
Ionizer
Radioactive
Ion
Beam
Low energy experiments
High energy experiments
Post-accelerator
Mass separator
Neutrals
Ions
Isobars only
Post-accelerated
18 m
20 cm
[pps]
10 - 50 m

## Slide 4
Target vs converter configurations
Extraction electrode
Target
T=2000 °C
Ionizer
RIB
Extraction electrode
Target
T=2000 °C
Ionizer
RIB
Spallation neutrons

## Slide 5
Concept history at ISOLDE
5
2003
Protons
Neutrons
A. Gottberg, et al., NIMB 336 (2014) 143–148.
R. Luis, et al., et al., EPJA 48 (2012) 90
Protons
Neutrons
2014
Target
(UCx)
Converter
(W rod)

## Slide 6
Spallation-driven, two-step RIB targets
Ramos et al., NIM B 463 (2020) 357–36
Tested online in 2018
Tested online in 2020, 2021, 2022
Target
(UCx)
Converter
(W rod)

## Slide 7
Target/converter optimization: Particle tracking
N-fiss: 1.45E11 [1/s]
P-fiss: 1.36E11 [1/s]
Parameters optimized:
Converter length (20mm)
UCx inner diameter (15 mm)
Converter position (after target)
Principle:
Physics goals
Monte Carlo (FLUKA)
[1/cm2/100μA]
Neutrons
Protons
ID
W length
UCx
UCx
W
UCx
UCx

## Slide 8
Target/converter optimization: FEA Thermo-mechanical
Optimization:
Leg shape  homogenize T in target
UCx outer diameter  Affects target Tmax
Principle:
Numerical FEA
Engineering design (CAD, component prototyping & testing)
Manufacturing, assembly, installation
Results:
Homogeneous target material temperature (ΔT~50°C)
Measured temperature ≥ simulated temperature

## Slide 9
Results:
Optimum W length = 2 cm
Power deposited = 7525 W
Tmax (W) = 1739 °C
Tmax (CuCrZr) = 360 °C
Tmax (H2O) = 149 °C
Plastic stresses OK
Converter optimization
Bolts for axial clamping
Water channels
Tungsten (W) converter
CuCrZr
brackets
Objectives:
Minimize thermal shine to target
 Active water cooling
Maximize neutron-induced fissions
 balancing power vs neutron production
Available conditions:
Flow H2O ~ 6 [lpm]
Pressure H2O ~ 6.8 [bar]
Tevap (H2O @ 6.8 [bar]) = 166 °C
Spring-loaded bolts
Creep resistant alloy CuCrZr
Thermal conductance through offline tests

## Slide 10
Online results at
ISAC-TRIUMF

## Slide 11
P2N improves production in n-rich region
Measured yield ratios P2N / ISAC-UCx
Neutron-Rich Improvement Factor (NRIF):
Quantifies P2N performance to enhance n-rich production.
Increased neutron-rich purity by 5x – 20x
NRIF
Conventional ISAC-UCx: In-target production (FLUKA)
Converter: In-target production (FLUKA)
Conventional ISAC: Measured yield
Ratios are half-life independent
Yields/μA P2N can take ~4x more p+ current
Converter: Measured yield
Chains measured for Cs, Rb, Sn, Zn
Data
Simulation

## Slide 12
Beam-independent temperature control
Trend comparable with ISAC-UCx
P2N release efficiency higher
  Temperature homogeneity
N-deficient efficiency > 100%
  P-beam mis-steered
Cs yields at lower temperature
  Temperature-controlled mode
  Enables cleaner Cs, Rb beams by suppressing n-deficient lanthanides by a factor ~1000
Target
Target
ISAC-UCx Target
P+ beam
Target
Spall neutrons
P+ beam
Target
Converter
Converter
Target
Target
ISAC-UCx Target

## Slide 13
Yield vs p+ intensity: Linearity
Neutron rich Cs
Neutron deficient Cs
Proton beam position likely changes when adjusting its intensity:
Inducing more spallation in annular UCx
Increased n-deficient production
Linear trend confirmed:
Temperature independence
Comparing yield/μA adequate
Confirms that yields can be presented per unit of primary beam [Yield/μA]
No Radiation Enhanced Diffusion noticed on broad p+ range

## Slide 14
A bigger proton beam size (FWHM) increases contaminants
Cesium
Rubidium
FWHM considerations:
Larger beam  Higher spallation on UCx from “beam tails”
Conservative operation of target module (Al6061) window:
  Ip+ (max) = 80 μA (@ FWMH = 4 mm)
  Ip+ (max) = 99 μA (@ FWMH = 7 mm)

## Slide 15
Post Irradiation Examinations (PIEs)
PIE observations
Converter always withstood beam power
Target windows broke only with Ip+ > 50 μA
SEM and EBSD performed on irradiated UCx at SCK CEN
  Carbides were oxidized due to air exposure
  UCx particle size grew ~10x

## Slide 16
TRIUMF accelerators
Muons for
material science
500 MeV – 400 μA
H- Cyclotron
PIF
STF
T1
T2
82Sr medical production
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
TR: 13
TR: 30-1
TR: 30-2
CP: 42
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from ~2025)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL1A
ITW
ITE
ISOL
(ISAC)
BL2A
BL2C
BL4N

## Slide 17
Converters for high-power RI Beam production
Protons
Electrons

## Slide 19
Backup

## Slide 20
UCx disc
Release in ISOL targets
Isobars only
Post-accelerated
10 μm
1 μm
UCx + C
After conditioning
1 μm
UCx + C
heated and irradiated
n-SiC
Electrospun
Extraction electrode
HV 60 kV
Target
T=2000 °C
2 kV
Ionizer
Radioactive
Ion
Beam
Neutrals
Ions
Isobars only
Post-accelerated
20 cm
;
Diff.
param

## Slide 21
Effect of beam windows on proton beam

## Slide 22
Target optimization process

## Slide 23
Target/converter optimization: FEA/prototyping
Optimization:
Leg shape  homogenize T in target
UCx outer diameter  Affects target Tmax
Converter shape  minimize temperatures in W/Cu
Principle:
Numerical FEA (ANSYS, thermal/electric/structural)
Engineering design (CAD, component prototyping & testing)
Results:
Homogeneous target material temperature (ΔT~50°C)
Converter T/stresses are compatible with online operation
Lateral surface
Central temperature
Electrical connections
TIG
torch

## Slide 24
Converter optimization - backup
Available conditions:
Flow H2O ~ 6 [lpm]
Pressure H2O ~ 6.8 [bar]
Tevap (H2O @ 6.8 [bar]) = 166 °C
Spring-loaded bolts
Creep resistant alloy CuCrZr
Thermal conductance through offline tests
Results:
Optimum W length = 2 cm
Power deposited = 7525 W
Tmax (W) = 1739 °C
Tmax (CuCrZr) = 360 °C
Tmax (H2O) = 149 °C
Plastic stresses OK
Temperature [°C]
Plastic strains [Pa]

## Slide 25
Cesium efficiency compared to ISAC-UCx historical

## Slide 26
Rubidium efficiency compared to ISAC-UCx historical

## Slide 27
Linearity: Yield vs p+ current
Linear fit:
Confirmation that yields can be presented per unit of primary beam [μA p+]
Confirms little thermal coupling between p+ and target windows
N-rich Cs isotopes used to suppress spallation contribution
Previous work
Radiation Enhanced Diffusion (RED) not seen in converter, yields are linear
Difficult to decouple it from thermal effects for high-power proton beams
ISOLDE yields from cold target show release higher than expected
ISAC enhancements might be thermally induced by the resistive heating adjustments
Ramos et al., https://doi.org/10.1016/j.nimb.2016.03.003

## Slide 28
Radiation Enhanced Diffusion (RED)
Hints of RED effect:
Looking at one target only
Target heater and proton beam current “compensate” each other to aim for a constant temperature.
Historical data through 25 years:
No data close to origin to confirm over-linearity
Yields drop after 60μA
Temperature effects difficult to disentangle

## Slide 29
MR-ToF (TITAN) results
Time split between yield measurements and MR-ToF measurements
  Assessing relative contaminant yields (50%)
  Measuring masses for relevant science cases (50%)
Maximum RIB current in MR-ToF ~ 106 pps
Purity gains enabled measurements of 10 new masses:
  83Zn, 149Cs, 150Cs, 151Cs, 151Ba, 152Ba, 136Sn, 137Sn, 138Sn and 86Ga
Molecular contamination reduced
85Rb
85Ga
P2N 2021
ISAC 2017
Mo
2H:2C12:59Co
2H:3C12:47Ti
85Br

## Slide 30
Assembly and online installation
Target
Converter
Graphite cartridge
Uranium carbide discs
Target module

## Slide 31
Many people involved at several levels:
At TRIUMF: Alex Gottberg, Pierre Bricault, Mia Au, Marla Cervantes, Fernando Maldonado, Ferran Boix-Pamies, Tom Day Goodacre, Carla Babcock, Peter Kunz, Friedhelm Ames, Andres Mjos, Aaron Schmidt, Jens Lassen, Ruohong Li, Ricardo Dos Santos Augusto, Darwin Ortiz Rosales, David Wang, Frank Song, John Langrish, Chad Fisher, Matthew Gareau, Navid Noori, Aurelia Laxdal, Sundeep Gosh, Arthur Leung, Joe Mildenberger, Max Kinakin, Maico Dalla Valle, Dan MacDonald, John Wong, TITAN team, TRIUMF Machine Shop, Vacuum, Controls, Mechanical Services Group.
At SCK CEN and ISOLDE: Joao Pedro Ramos, Donald Houngbo, Jarno Van de Walle, Lucia Popescu, Marc Dierckx, Santiago Ramos Graces, Sebastian Rothe, Thierry Stora.