## Slide 1: Status and R&D of the target and beam dump at FRIB
J. Song, M. Reaume, N. Bultman, M. Patil,
R. Quispe-Abad and J. Wei

## Slide 2: Targetry Systems Overview
Target and beam dump for the experiments of PAC01 and PAC02
  Single-slice rotating graphite target
  6⁰ S-shape static beam dump
  In FY2023, the primary beam power was operated a 5 kW
  The 10kW operation has just started with a 28Si beam to produce the 25Al beam
    Primary beams: 18O, 28Si, 36,40Ar, 64Zn,124Xe,198Pt and 238U
Single-slice Target
Static Beam Dump
Target Vacuum Vessel
Beam dump Vacuum Vessel
~ 200MeV/u
Beam
More than 210 Rare Isotope Beams Delivered to FRIB User Experiments for Year 1
~25% heat deposit
~75% heat deposit
~ 150MeV/u FOI
FRIB Accelerator System
Primary beam acceleration
Fragments of Interest Production
User experiments

## Slide 3: Power ramp up plan: Target System
1 kW
40 kW
400 kW
Static target
Single-slice
Multi-slice
10 kW
we are here

## Slide 4: Current Production Target
Single slice target
Criteria for determining the maximum beam power
  Graphite disc temp. < 1900 0C
  Bearing temp. < 150 0C, New(NSK) bearing < 230 0C
  Moresco Lubricant temp. < 250 0C
Radiation cooling
Primary beam size: = 0.25 mm
Rotating speed: currently operating at 500 rpm
Disc
  Single slice
  Mersen Graphite, grade 2160
  grain size: 5 μm, density: 1.86 g/cm3
  Assumed ε=0.85
  thickness: 1.2, 2.1, 3.5, 5, 8, 10, 15 and 18 mm
HX
  Cu
  Emissivity coating done, ε>0.6
Water cooling
  Inside, Front and Rear Doors
High emissivity coating, Jul. 2023
DPA < 0.05 after 10 kW a week operation
  Max temp ~ 800-900 C
  Can be used multiple times
No temp monitoring system

## Slide 5: Target defect, emissivity and offline test
Target defect
  Arising from machining tolerances, inhomogeneities, deformations, and etc.
  Requirement: 2%
  Current measurement (with beam) using a wedge viewer revealed that the target defect: 1.6 %
Thickness measurement
  Currently 5 points measurement with a micrometer
  Developing a device for continuous non-contact thickness measurement
Emissivity measurement
  Developing a device
  IR camera: RT – 1200 C
  Heater temperature: RT to 580 C
Offline target system test
  Developing a test system to perform
  offline thermal test on the target system
Referred to C. Zhu et al., “An accurate instrument for emissivity measurements by direct and indirect methods”

## Slide 6: Target temperature measurements and power limit
Latest experiment (11/2/2023)
  ~10 kW 28Si beam with 155 MeV/u on an 8 mm thick graphite target
  Temp distribution measured using a thermal imaging system
  Max temp on graphite disc
    887 0C (measured), 885-854 0C (simulation, HX )
  △T ~ 60 0C
Power limit
  With assumptions with =0.6 and utilizing low temp. bearing.
  The bearing operates within the operational temp limit, even for the extreme case of primary beam power of ~ 20 kW
500 W 28Si beam on stationary target
9.6 kW 28Si beam on rotating target
TIS
5 mm
Chart: Target temperature

## Slide 7: Multi-slice disc
Multi-slice target
  A prototype graphite discs have been fabricated for the 238U
  will require the total disc thickness to be ~ 1.2 – 2.1 mm
  The disc comes in two thickness: 0.6 and 0.4 mm (~3 slice discs)
    Mechanical tolerance ranges from 8 to 12 um
Thin poco graphite (AXF-5Q) discs

## Slide 8: Power ramp up plan: Beam dump
Primary beam
Mini-channel
Water cooling
Rotating drum
Primary beam
Water cooling
1 kW
30 kW
400 kW
20 deg static
6 deg static
Rotatable
10 kW
Mini-channel static
10 kW
we are here

## Slide 9: Beam sizes on beam dump
The varying beam sizes on the beam dump, depending on experiments or optics, make it challenging…

## Slide 10: Current Beam dump
Criteria for determining the maximum beam power
  Al plate temperature < 200 C
    The max stress reaches 185 MPa at 194 C and a criterion has been conservatively set not to exceed a yield strength of 200 MPa at 205 C
  Water temperature < 130 C
    Set not to exceed the boiling point of water at 3 bar.
Conditions
  Flow rate: 60 gpm
  Pressure drop: 0.63 psi
  Average speed: 2.4 m/s
  Average Heat transfer coefficient: 8800
DPA
  ~ few dpa per a week

## Slide 11: Beam dump thermal image
Thermal image of the beam dump
  A thermal camera is installed last spring
  Thermal image of the beam dump during the 10kW run
  The IR camera Temperature will be calibrated
Beam dump after 1 year of 3-5 kW beam operation

## Slide 12: Mini-channel Beam dump
Primary beam
Minichannel Water cooling
MCBD
  The primary beam stops at the minichannel beam dump
    Penetration depth < 1mm
  Beam intercepting plate
    CuCrZr/Al2219 (bimetal)
      Thickness: Cu (15 mm), Al (5 mm)
    Minichannel
      water channel (2mm) wall (2mm)
  Why CuCrZr?
    High thermal conductivity (320 W/m*K)
    High yield strength (380 - 550 MPa @RT)
    High radiation resistance
    Reference
      K. Yoshida et al., High-power beam dump system for the BigRIPS fragment separator at RIKEN RI Beam Factory NIMB 317 (2013)
      A. Cackett et al., Effects of radiation damage and precipitate distribution on micro-pillar compression testing of irradiated CuCrZr Journal of Nuclear Materials 553 (2021)
2mm width minichannel
Al2219
Water Supply
Water Return
CuCrZr
MCBD
  Criteria
    CuCuZr < 300 C, Al2219 < 200, Water < 130 C
  Flow rate: 60 gpm
  Pressure drop: 29.1 psi
  Average speed in the mini-channel: 8 m/s
  Average Heat transfer coefficient: 30,000
Radiation damage
  For 238U, peak DPA per a week for a 10kW operation, < 10 dpa

## Slide 13: Rotating Beam dump
Concept
  Beam stops in the water
    Easy to remove the heat
    Reduce the radiation damage
Current issues
  Water seal development
    Lip seal
    Ferrofluid seal
  Increasing a beam dump head height to cover multiple charge states of 238U beam
Water leak after couple of hour operation

## Slide 14: Summary
Target
  Single-slice
  Multiple-slice
Beam dump
  6 deg Beam dump
  Mini-channel beam dump
  Rotating beam dump
10 kW beam power available at FRIB now
Thank you for your attention!

## Slide 15: Backup slide
Thermal analysis results
CuCrZr, max stress is 304 MPa at 327 C, which is close to the yield strength of Cu alloy at 327 C, ~ 330 MPa.
Al2219, max stress is 161 MPa at 160 C, which is lower than the yield strength of Al alloy at 160 C, ~ 230 MPa.
Stress analysis results

## Slide 16: Acceptance Criteria
Maximum allowable temperature in Cu and Al plates, are 300 and 200 C, respectively.
CuCrZr < 300 C
Chart: All2219-T851
| 24 | 100 | 150 | 205 | 260 | 315 | 370
Yield strength (Mpa) | 345 | 324 | 276 | 200 | 159 | 41 | 26
Tensile strength (Mpa) | 455 | 414 | 338 | 248 | 200 | 48 | 30
Al2219 < 200 C