## Slide 1: HiRadMat: a high power targetry facility at CERN
A. Goillot, A. Ebn Rahmoun, P. Simon, V. Stergiou, E. Andersen, N. Charitonidis
10th November 2023 – HPTW2023

## Slide 2: Outline
HiRadMat facility
Expertise provided to users
Highlight of experiments
Upgrade works
Transnational access

## Slide 3: Introduction
The CERN accelerator complex, layout in 2022. © CERN
Commissioned in 2011
Testing especially LHC components
Share the same SPS extraction line
High intensity instantaneous high-power beam
Study material properties
Worldwide scientific community
HiRadMat: Short-pulse high-energy proton irradiation facility

## Slide 4: HiRadMat, a flexible facility
 | Protons | 208Pb Ions
Beam Momentum | 440 GeV/c | 173.5 GeV/n (36.1 TeV/ion)
Pulse Energy | up to 2.4 MJ | up to 21 kJ
Bunch Intensity | 5·109 – 2.3·1011 protons | 3·107 - 7·107 ions
Number of Bunches | 1 to 288 | 52
Maximum Pulse Intensity | 3.46 · 1013 protons | 3.64 · 109 ions
Bunch Length (4 sigma) | 1.5 ns | 1.5 ns
Bunch Spacing | 25 ns | 100 ns
Beam Size at Target | ~ 1 mm2 | ~ 1 mm2

## Slide 5: HiRadMat, a flexible facility
Beam Diagnostics
Transverse spot size
Bunch-to-bunch beam position
Beam losses
Test Stands
Remote plug’n’play
~300 signal connections
Cooling water, vacuum, press. air
Maximum flexibility to accommodate any request
  Experimental stands
  Shielded areas to protect electronics
  Beam parameters
TNC – Irradiation area
TT61 – shielded area
Injection from SPS

## Slide 6: Operation schedule
HiRadMat commissioned
2021 - 2025
2011 - 2012
Operation
2013 - 2014
2015 - 2018
Long Shutdown 1
Operation
2019 - 2020
Long Shutdown 2
Long Shutdown 3
2026 - 2028
Experiments
16 Materials R&D
11 Accelerator component prototyping
6 Targetry R&D
9 Beam diagnostics
2 Particle detectors
2 Plasma Physics
60 publications
Future experiments
High Lumi LHC program
DPA theory research
Plasma physics for astrophysics phenomena
ATLAS detector test
Also look for more

## Slide 7: Timeline of experiment in HRMT
Initial phase
  A first idea for an experiment arises somewhere in the world
  Feasibility and time-line judged through initial discussion with HiRadMat team
  Consultation / meetings between various experts at CERN or remotely
Preparatory phase
  Experiment maturing: Scientific Board (scientific merit)
  (if OK): Technical Board (technical feasibility and safety)
  (if OK): experiment gets in the draft schedule of next year
Experimental phase
  Beam time approval (protons) by the CERN ATS sector executive committee (IEFC)
  Beam time allocated
  Experiment performed
Post irradiation phase
  Post irradiation analysis
  Follow up of… Results presentation meetings, or small workshops

## Slide 8: Expertise provided to users
Experiment preparation
3D integration & mechanical studies
Installation & survey
Transport and handling
On-line diagnostic equipment and expertise
Sensors, Cameras & LED
Movable stages (H&V)
Remote control of the equipment
Beam diagnostics
Beam parameters
Automatic parameter display
Auto-logging in CERN infrastructure

## Slide 9: Outline
HiRadMat facility
Expertise provided to users
Highlight of experiments
Upgrade works
Transnational access

## Slide 10: RaDIATE (2022)
Investigate thermal shock behaviour of beam-intercepting materials in support of current and future multi-MW accelerator target facilities and experiments
  Motion stages (H&V)
  LDV / Strain gages
  LED + Rad-hard camera
  Specimen disassembly in bunker
Experiment in 2025 (See talks of F. Pellemoine and K. Ammigan)
On courtesy of Kavin Ammigan (and RaDIATE Collaboration)

## Slide 11: HED (2021)
Validating design of the future HL-LHC External Beam Dump core
  Size of the chamber
  77 pulses in total at highest intensity (~2.6x1015 protons)
Follow up experiment planned for 2024
  Higher energy density (1.8e11ppb)
  Under argon
  One shot yielding accidental scenario
See talk M. Calviani for HL-LHC dump upgrade
On courtesy of Gabriel Banks and Pablo Andreu Muñoz (and the SY-STI-TCD section)
Beam parameters:
440 GeV / 1.1e11 ppb
HRMT-56 tank CAD model
beam

## Slide 12: SC Coils (2022)
Identify damage mechanisms in multilayer, impregnated coils due to instantaneous beam impact.
Cryogenic tank for low temperature (2nd experiment of this kind)
Diamond beam loss monitors
Temperature sensors
Heater
Motion stages (H&V)
Cooling water system
On courtesy of David Gancarcik (and the TE-MPE group)

## Slide 13: FIREBALL (2023)
On courtesy of Charles Arrowsmith (and the FIREBALL collaboration)
Produce a laboratory analogue to an electron-positron enriched astrophysical jet
  Complex experiment with various equipments (Faraday rotation probe, Rad-hard cameras, sensors)
  Fluka simulations for optimising shielding and background
  Production of e-/e+ and electro-magnet (MNPA) as particle energy spectrometer
New experiment in 2024
C. D. Arrowsmith et al. (2023) "Inductively-coupled plasma discharge for use in high-energy-density science experiments" Journal of Instrumentation 18 04 P04008. 10.1088/1748-0221/18/04/p04008
Notes: publications

## Slide 14: Upgrade works
Increase intensity (accelerator complex upgrade)
Beam line and dump window failures
HiRadMat Facility Upgrade Study Group
  Machine
  Infrastructure
  Beam dump
 Works for upgrade

## Slide 15: Upgrade works
Partition of the beam line vacuum sector
  Be  glassy C
  To separate this chamber from the extraction line
  Vacuum recovering easier
Beam dump
  Extension of the collimator
  Make replacement of window easier in case of damage
Beam diagnostic
  New downstream BTV
  Beam angle
Injection from SPS
TJ7 bunker
TT61 – shielded area
TNC – Irradiation area

## Slide 16: Transnational Access
Funding of the mobility of international teams to come at CERN for collaboration
  Preparation of the experiment
  Installation time
  Beam time
Supported more than 20 external users during 240 days of transnational access during one operational year
GB

## Slide 17: Remember
Single pulse high-energy proton facility for targetry test (or other…)
Flexibility
CERN environment -> technical and scientific support
Offer transnational access
hiradmat-operation@cern.ch
https://hiradmat.web.cern.ch/
Look for more collaborations!

## Slide 18
A big thank you to all the groups along the ATS sector for their dedication and help in the operation of HiRadMat facility since 2011!
SY-STI
SY-BI
BE-GM
HSE-RP
SY-ABT
BE-OP
EN-HE
BE-EA
EN-MME
TE-MPE
BE-CEM
BE-ASR
ありがとうございます !

## Slide 20
This project has received funding from the European Union’s Horizon Europe Research and Innovation programme under Grant Agreement No 101057511.

## Slide 21
Courtesy of S. Gilardoni (SY-STI)

## Slide 22: TPSG4-2 (2023)
Test the MSE protection element (diluter) in case of accidental shot and validate the simulations
6 tons of equipment
Exceptional size
Under vacuum and cooled down with water system
On courtesy of Cedric Baud (TE-ABT)
TPSG4 diluter
Protection element
MSE
Magnet

## Slide 23: Layout HiRadMat
Surface lab
Control room
Tunnel infrastructures
Injection from SPS
TJ7 bunker
TT61 – shielded area
TNC – Irradiation area

## Slide 24: Experiment preparation
Integration in 3D layout
Mechanical evaluation
Assembly
Installation
Survey (alignment precision < 1 mm)
Handling and transport
Disassembling
Notes: Split and less crowed and same bullet size

## Slide 25: Beam diagnostics
Beam TeleVision
Beam Current Transformer
Beam Position Monitor
Bean Loss Monitor
Vistar and logging automatisation for each shot
HiRadMat vistar
HiRadMat auto e-logbook

## Slide 26: Flexible software for users
Interface for motor stage control:
  DC stage
  Step-motor stage
Beam based alignment automatisation
Data acquisitions (temperature, cameras, pressure…)

## Slide 27: Partition of TT66 Vacuum Sector [TE-VSC]
In 2021 Be window failed twice: very expensive and long order delay
Material: Be window  glassy C
Vacuum sectorisation: one vacuum chamber VCAG.660410  two smaller chambers

## Slide 28: Dump upgrade [SY-STI]
Dump window not easily accessible and lies behind the collimator  difficult to fix during beam time failure
Situation after upgrade:
Dump entrance tube extended, the window will be accessible without any equipment removal
Addition of easily movable shielding in front of the collimator window
+ BPKG relocalisation

## Slide 29: Vacuum upgrade
Valve controller
Gauge controller
Experiment Table 3
Experiment Table 2
TT66
BTV.660518
BTV.660528
Gauge
Gauge
Gauge
Control valve
Control valve
Control valve
Primary pump
Primary pump