## Slide 1: Topic 8 (Multipurpose use of targets and beam dumps)
Hiroki Okuno Convenor of TOPIC8
2 invited talks and 2 contributed talks
Only one talk for multipurpose use

## Slide 2: Overview of the session 1
Invited talk
The Muon Collider Study: Challenges and perspectives
Roberto LOSITO (CERN)
  Muon target for Muon Collider
Production of astatine-211 for targeted α-particle therapy at RIBF
Hiromitsu HABA (RIKEN)
  Target for mass production of At211

## Slide 3: Overview of the session 2
Present status and upgrade plan of RI production target in SCRIT electron scattering facility
Yasushi Abe (RIKEN)
  RI production target for SCRIT
The ISAC facility secondary irradiation and PIE upgrades
Ferran Boix Pamies (TRIUMF)
  Secondary irradiation

## Slide 4
8th High Power Targetry Workshop, 6-10 November 2023
Challenges in the Design of Muon Colliders
R. Losito
for the International Muon Collider Collaboration
Co-Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

## Slide 6: Target System & shielding
6
Shielding (Tungsten)
HTS
Neutron absorber (water and boron carbide layer)
Target Titanium vessel
Stainless Steel wall
Cooling Helium
Titanium Outer Vessel
Vacuum
170
590
171
548
Static Helium
150
R15
C-Target
800
P+ Beam
Target He coolant (RT)
Shielding He coolant (RT)
Thermal Radiation shield
Stainless Steel Shielding vessel
water moderator
Target p+ beam pipe
Non cooled shielding
To be optimized with WP4 & WP7
Inside solenoid cryostat
Outside solenoid cryostat

## Slide 7
Production of astatine-211 for targeted α-particle therapy at RIBF
Hiromitsu HABA (RIKEN)

## Slide 8
0
50 [mm]
AVF
29-MeV 4He
25 pμA
N. Sato et al., RIKEN Accel. Prog. Rep. 50, 262 (2017).
S. Yano et al., RIKEN Accel. Prog. Rep. 50, 263 (2017).
Y. Wang et al., RIKEN Accel. Prog. Rep. 53, 192 (2019).
H. Haba, Drug Deliv. Syst. 35, 114 (2020) (in Japanese).
10o
Metallic 209Bi target
Purity: 99.999%
Thickness: ~20 mg/cm2
12 mm
69 mm
Development of production technology of 211At at AVF
Water- and helium-cooled target chamber
Dry distillation of 211At
850oC
PFA trap cooled with C2H5OH at –100 oC
Oxygen
200 μL of H2O, CH3OH, CHCl3, …
(Chem. Yield: ~80%)
Be vacuum window (20 μm)
Cooling He (30 L/min)
29-MeV α beam (25 pμA)
209Bi target
(~75 mg/cm2)
Cooling water (4 L/min, 5oC)
Beam energy monitor
(TOF detector)
→ 29 (±1%) MeV
Beam wobbler
(2 Hz, φ3 mm)
25 pμA×1 h → 1.2 GBq of 211At (EOB)
Al plate (1 mm)
Metallic Bi
M.P.: 271.5oC
T.C. (300 K): 7.97 W/m⋅K
T. Watanabe et al., Proc. of PASJ12, 1198 (2015).

## Slide 9
Development of a large-scale 211At production apparatus
Rotating liquid Bi target
Heat the vessel to dissolve Bi at 300∼400°C
Spread Bi to the wall of the vessel by centrifugal force
Rotation at 2000 rpm
FY2017–

## Slide 10
RIKEN Ring Cyclotron
・Irradiation with 28-MeV × 25-pμA 4He beam
・High recovery yield (∼80%), comparable to that of conventional apparatus
・Production of ∼200 MBq of purified 211At required for a typical use after 1.5-h irradiation
211At production chamber
4He beam
Commissioning of the large-scale 211At production apparatus
29-MeV
25-pμA 4He
29-MeV
25-pμA 4He
RILAC2

## Slide 11
SRILAC
211At
28 GHz ECRIS
Development of production technology of 211At with 100-pμA 4He beam
–
211At
Future plan: large-scale production of 211At at SRILAC
Nucl. Chem. Lab.
RI production beam line under construction
Large-scale 211At production apparatus
GARIS III
SHE RIs
SRILAC
(2020.1~)

## Slide 16: The ISAC facility secondary irradiation and PIE upgrades
Ferran Boix Pamies and Alexander Gottberg
HPTW 2023

## Slide 17: ISAC-TRIUMF
ISAC RIB production target
ISAC target station
RIB
H+

## Slide 18: Multipurpose use of ISAC targets
Operational fluxes near ISAC targets
20day, 1kW irradiations of secondary targets are considered readily achievable with existing infrastructure
In-beam radiation damage
Off-beam radiation damage
Long-lived radioisotope production

## Slide 19: Secondary irradiation development
24
(mm)
3
SPT samples
Ø=4
THK<1
Ø=56
THK=7
Future ARIEL targets aim to use coaxial spring-energized PEEK seals
In parallel, PEEK SPT samples are irradiated to similar doses
The assembly can be leak checked post-irradiation in the hot-cell
In-beam secondary target
Off-beam secondary assemblies

## Slide 20: Secondary irradiation campaign
week\month | June | July | August | September | October | November | December
1 |  | UC#33 ST#2 | Ta#62 ST#3 | UC#34 | Shutdown | UC#35 | Ta#63 ST#5
2 |  |  |  |  | Shutdown |  | 
3 | UC#32-p2n ST#1 |  |  | SiC#41 ST#4 | C#3 | UC#36 | 
4 |  |  |  |  |  |  | 
week\month | June | July | August | September | October | November | December
1 | UC#37-p2n | Ta#64 ST#7 ST#8 | UC#38 | SiC#44 | Shutdown |  | UC#41
2 |  |  |  |  | Shutdown |  | 
3 | SiC#43 ST#6 |  |  | UC#39 ST#9 | C#4 ST#10 ST#11 | UC#40 ST#12 | 
4 |  |  |  |  |  |  | 
week\month | June | July | August | September | October | November | December
1 | TiC#5 |  | UC#42 | Nb#11 ST#15 | Shutdown |  | 
2 |  |  |  |  | Shutdown |  | 
3 | TiC#6 | TiC#6 |  | Ta#65 |  |  | 
4 | SiC#45 ST#13 ST#14 |  |  |  | Ta#66 | UC#43 | 
2021
2022
2023
Secondary target # | Material | Total charge (mAh) | DPA-NRT max. | DPA-FLUKA max. | He (appm) max. | H (appm) max.
ST#1 | Al6061, AlSi10Mg (AM) | 2.9 | 0.025 | 0.014 | 8 | 10
ST#2 | Al6061, AlSi10Mg (AM) | 33.3 | 0.48 | 0.28 | 142 | 190
ST#3 | SS316L, CrMnFeCoNi (HEA) | 40.6 | 1.76 | 0.77 | 187 | 530
ST#4 | SS316L, CrMnFeCoNi (HEA) | 11.8 | 0.46 | 0.28 | 44 | 125
ST#5 | CrFeCoNiCu (HEA), CrMnFeNi (HEA) | 13.9 | 0.51 | 0.23 | 42 | 117
ST#6 | CuCrZr | 79.0 | 5.99 | 2.58 | 417 | 1135
ST#7 | SS310, 800H | 22.7 | 0.87 | 0.38 | 86 | 256
ST#8 | Cu (AM) | 22.7 | 1.31 | 0.57 | 90 | 246
ST#9 | Al6061 | 4.2 | 0.05 | 0.03 | 16 | 21
ST#10 | SS316L | 28.8 | 1.88 | 0.81 | 223 | 629
ST#11 | Al6061 | 28.8 | 0.44 | 0.24 | 136 | 182
ST#12 | SS316L | - | - | - | - | -
ST#13 | Ta (AM) | 45.2 | 3.13 | 1.09 | 292 | 373
ST#14 | TRISO, Ni-alloys | 45.2 | 2.7 | 1.19 | 254 | 909
ST#15 | ZrC | 27.0 | 1.34 | 0.54 | 98 | 187

## Slide 21: Post-Irradiation Examination
Characterization tools:
Mechanical: Actuator up to 4.5kN, Small punch test stage
Microscopy: TEM (not yet commissioned), SEM
Others: Thermal conductivity, isotope release studies
Access to additional characterization tools and sample preparation with CNL
Arunkumar, S. Met. Mater. Int. 26, 719–738 (2020).
Plan for PIE laboratory
Punched SS310 samples
SPT technique

## Slide 22: Outline
Results: FeCrMnCoNi vs SS316L
  Mechanical characterization
  TEM analysis, preliminary

## Slide 23: Future work
  Collaboration with Canadian Nuclear Laboratories (CNL)
  Development of a temperature control stage
  High temperature irradiations (~1000degC)
Cement embedded TRISO particles
  PIE
  Development of PIE lab
  TEM installation
  ISAC Al6061 beam windows
  Two windows recovered:
  6.5 DPA-NRT, 2050 appm He
  9 DPA-NRT, 2830 appm He
  ARIEL
  Secondary irradiation positions available
R.S. Augusto et al., Radiation Physics and Chemistry 201 (2022) 110491