## Slide 1: ZDC Detector Technology Choice
RIKEN
Itaru Nakagawa

## Slide 2: eRHIC Forward Magnet Apertures
B0PF
Q1PF
C1XPF
Q2PF
B1PF
B2APF
B2BPF
Q0EF
Q1EF
ZDC
Forward Side
Spectrometer Dipole
Roman Pot Region
Closest Large Aperture, High Field Quadrupole

## Slide 3: Compact Forward Magnet Example
Direct Wind, NbTi, Actively Shielded eRHIC Q1PF
X (mm)
BY (T)
Main Coil
Shield Coil
Zero Field Region
Q1PF By Field
Rapt = 55 mm
Efficiency Factor = 90%
Gnet @ 275 GeV = 80.8 T/m
Budget for outer structure was set to accommodate the electron beam pipe.
Forward magnets must have large apertures to accommodate neutrons and forward charged particles.
But combination of large aperture and large gradient mean a large B-field at the coil....
However, the electron beam must be shielded from any large external fields.
“Pole Tip Field” = 4.4 T
Quad Field
Return Flux

## Slide 4: Shielding e-Beam Inside Spectrometer Dipole
B0 Magnetic Yoke
Superconducting Coils
e-Beam
Magnet is aligned with the e-beam, so p-beam enters at 25 mrad angle.
Experimental
Detector Here
1.3 T Cancel Coil Detail
Q0EF
B0PF/Q0EF
eRHIC IR needs to pass an e-beam through main aperture of first hadron spectrometer dipole (B0PF).
First electron quad (Q0EF) inside B0PF.
With a combination of a bucking dipole and passive shielding, this can be accomplished.

## Slide 5: Detector Beam Pipe
Small diameter, thin walled Be in center region.
Smooth tapers and transitions to limit energy deposited by beam in trapped modes (wakes).
Need to provide beam tube cooling and Higher Order Mode (HOM) absorbers.
Need to provide adequate vacuum pumping.
eRHIC / Beast plans include in situ bakeout.
Central beam pipe requires meticulous optimization.

## Slide 6: Detector Idea?
2~3Xrad
Low Energy Section?
Hcal Extension
Shower Max Choices | Radiation Hardness | Cost | Position Resolution | Experiments
Quartz Fiber | good | Inexpensive | Poor | ALICE, JZCaP
Scintillator Fiber | poor | inexpensive | OK | RHICf
Silicon Sensors | OK | Expensive | Best | RHICf, FoCAL, TOPSiDE
Sampling Type EM Section

## Slide 12: Discussion with Mike Murray
About EM Section of ZDC Upgrade

## Slide 13: ALICE ZDC

## Slide 14: ZDC detector
Electromagnetic section (EM):
  33 vertical tungsten plates
  19 radiation lengths or one nuclear interaction length.
  5 divisions in the x direction
    (Not enough room for read-out of y-segmentation)
Reaction Plane Detector (RPD):
  4x4 quartz block array
Hadron section (HAD):
  24 tungsten plates
  5.6 hadronic interaction lengths
  Plates are tilted by 45◦ → maximizes the light that a ﬁber can pick up.
  Divided into 4 segments in z direction
Notes: Em 2 mm thick 1.5 cm for had plates 1 cm quartz rpd

## Slide 15: Segmentation of ZDC detector
Segmentation:
  EM: x-axis – 5 channels
  HAD: longitudinally – 4 channels
  RPD: 4 x 4 quartz array – 16 channels
Physics capabilities:
  Centrality in pA, AA
  Tagging UPC events
  Event plane (with RPD)

## Slide 16: Quartz Fibers

## Slide 17: TOPSiDE

## Slide 18
Measure (E,x,y,z,t) for (every) hit in tracker + calorimeter
Silicon pixel vertex + strip tracker
Imaging em calorimeter
Imaging hadron calorimeter
Superconducting solenoid (3T)
Forward gaseous RICH
Forward dipole + cloak or
toroid w/out cloak
Forward silicon disks
Forward calorimetry
Zero degree calorimeter
Backward silicon disks
Backward crystal calorimeter
Particle identification ( pion – kaon – proton separation)
Particle momenta < 10 GeV/c for most of the solid angle f
Utilizes tracker + calorimeter
Requires silicon sensors with time resolution of about 10 ps*
Eliminates
The need for preshower counters, TRDs, TOF or Čerenkov (in front of the calorimeter),
muon chambers (in back of calorimeter)
: The 5D Concept
Particle identifying
imaging
calorimeter
*3 timing layers are sufficient:
early in the ECAL, rear of ECAL,
rear of HCAL:
A resolution of 20 ps is then
adequate. (TBC by simulation)

## Slide 19
Role
Requirements
Dimensions: Laterally ~ 1 x 1 m2 (to contain hadronic showers)
Longitudinally at least 5 interaction lengths
Event rate (not exorbitant?)
Timing resolution (not particularly challenging?)
Radiation hardness (not a concern?)
Energy range 100 – 200 GeV (EIC) and 7 TeV (LHeC)
Choice of technology
Electromagnetic Calorimeter ECAL
A) Silicon wafers → Si-W technology
Hadron Calorimeter HCAL
B) Scintillator pads → AHCAL technology
C) Resistive Plate Chambers → DHCAL technology
The Zero-degree Calorimeter
Measure energy and angle of straight going neutrons
Identify (measure) the occasional photon in the calorimeter
All explored by

## Slide 20
A) The Silicon – Tungsten Electromagnetic Calorimeter – Si-W ECAL
Concept
0.5 x 0.5 cm2 Silicon pixels on 325 μm thick wafer
Tungsten absorber plates (< 1 X0 each)
Readout
Digitization implemented in each layer
64 channel SKIROC ASIC with 12 – bits
Low noise (1/10 of a MIP)
Option to power pulse (25 μW/channel)

## Slide 21
Linear within ±1% up to 45 GeV
Resolution adequate
-> Negligible contribution to σ(Ejet)
Excellent agreement with GEANT4 simulation
Si-W ECAL Results from Physics Prototype
Both concept and technical implementation validated

## Slide 22
A step further: the 5D concept
Precision timing information
Of order 10 picosecond
In addition to imaging capability
Advantages
Provides particle identification (pion-kaon-proton separation)
Identifies vertex in pile-up events
Suppress noise
Requires
Ultra-fast silicon detectors (UFSDs)
Sensors with 16 ps resolution available
Argonne: implementation of readout electronics onto sensor
→ reduce cost and further improve resolution
Time difference from a pair of sensors
[ps]
Measurement
at room temperature
with DAQ by scope

## Slide 23
C) The Digital Hadron Calorimeter - DHCAL
Concept
Resistive Plate Chambers (3 layer to obtain 1 m2)
Steel absorber plates (~ 1 X0 each)
Readout
Digitization implemented in each layer
64 channel DCAL ASIC with 1 – bit (digital!)
Timing to ~ 100 ns

## Slide 24
DHCAL Physics/Technological Prototype
38 layers in main stack – 4 interaction lengths deep
14 layers in tail catcher – additional 4 interaction lengths deep
Tests in Fermilab (Steel) and CERN (Tungsten) test beam

## Slide 25
Talking about neutrons…
High energy neutron events
Recorded at Fermilab in self-triggered (streaming) mode
Energy unknown

## Slide 26: Summarry of Discussion with Oleg
2019/10/02
Attendee: Oleg, Yuji, Ralf, Itaru

## Slide 27: Suggestions from Oleg
For mini-FoCAL position layers, options can be:
  Scintillation fiber
  Silicon sensors : existing detector is MPC-EX@PHENIX
Existing detectors uses scintillation fiber:
  LHCb tracker (TDR should be available) the detector can be already built
  STAR event plane detector (EBD). Can possibly learn how to connect the scintillation fiber to a clear fiber to transfer the photon to the front end electronics. Contact with EBD expert.

## Slide 28: Rough Cost Estimate
Diameter 1.0mm x 2m long round fiber = $3.96/piece
Each shower max layer, we need 1.0mm x 1.0mm square x 100mm long x 100 fibers to cover 10cm wide.
For two layers, 100 x 2 layers = 200 fibers.
The square shape is a bit more expensive than the round one, so assume $20/fiber even it is shorter.
200 fibers x $20/fiber = $4k/xy-layer
Oleg’s estimate for ~$5k (SiPM) + ~$5k (pre-amp). So the total is $4k + $5k + $5k = $14k.

## Slide 29: Kuraray

## Slide 30: Choice of Fibers
 | SCSF-3HF | Blue Fiber
Radiation hardness | good | weak
Light Emission | weaker | stronger
Suitable Use | Shower max | Energy sampling layers
For one year dedicated low luminosity run, the blue fiber may be OK. If we consider about future use, then may be worthy to consider SCSF-3HF.

## Slide 31
STAR EPD

## Slide 32
LHCb Fiber Tracker

## Slide 33: LHCb Fiber Tracker
The modules will have 2.5m long scin- tillating fibres with a diameter of 250 μm. The fibres will be read out by Silicon Photomultipliers (SiPMs) contained in Read-out Boxes at the top and bottom of the detector.

## Slide 34: Other Detectors

## Slide 35: psTOF for the EIC at 0°
Mickey Chiu

## Slide 36: Some Other TOF Technology Today
RD51 supported PICOSEC has achieved ~25 ps
MCP-PMTs have been shown to be capable of ~5 ps since 2006 (K. Inami et al), but for very few channels, and at very high cost
  LAPPDs as a possible solution?

## Slide 37: Example Design of a Very Forward psTOF
Similar design to QUARTIC detector proposed for the LHC
Rad-hard, High Rate Design

## Slide 38: How Well Can psTOF Measure A and Z?
Mass M (A – BE in the case of Ions)
Charge Z
PZ
PT
t ~ 120 ns, 𝛾 ~ 100 → dt ~ 0.1 ps for dM/M ~ 1%
Num. photoelectrons (1 cm fused silica radiator and LAPPD MCP-PMT Gen1 design):
319K ± 565, Z = 79
311K ± 557, Z = 78
Also means that in principle, the timing resolution one can achieve for the LAPPD (50 ps TTS) is
50 ps/√NPE = 0.1 ps!
Measured by magnetic spectrometer