## Slide 1: Progress report
Kosuke Tsukui

## Slide 2: MRPC
260 μm×5 gaps×2 stacks
8 strips / module
Gas : R134a (Freon) 90%, SF6 10% (quench gas)

## Slide 3: Set up
beam
MRPC
Dipole magnet
Target: Lead
0.55 mm thick
UPveto
Scinti.
Electron
30 cm
〜2.4 GeV
1GeV
trigger size : 2 1 cm
  trigger scinti : 10 1 cm ・ 7 2 cm

## Slide 4: Result
Dark current of RPC
200 mV/div, 4.00 ns/div

## Slide 5: Result (RPC1)
RPC1 Strip4
Hit position : center
Time resolution : 72.4 0.5 ps
Efficiency : 96.9 0.9 %

## Slide 6: Result (RPC2)
RPC2 Strip3
Hit position : center
Time resolution : 81.5 0.7 ps
Efficiency : 64.2 0.7 %

## Slide 7: Slewing
Slewing correction

## Slide 8: Back up

## Slide 9: Time Over Threshold method
threshold
Measure pulse width that exceeds the threshold.
Slewing correction using the signal width instead of the signal charge.
Pulse charge
Pulse width

## Slide 10: HR-TDC using FPGA
Delay
D-FF
Clock
Hit
Delay time is 5 – 30 ps
Clock frequency is 520 MHz

## Slide 11: HR-TDC using FPGA
Tapped delay line
Remapping (192 -> 64 taps)
Leading edge finder
Binary encoder
Clock domain crossing
Calibration table
Event build process
520 MHz
130 MHz
1111111111111100000000000000
1111100000
0000100000
5 : Fine count