## Slide 1: FPHX Readbacker Development
April 23, 2021 Miu Morita, Yumika Namimoto, Mika Shibata, Runa Takahama, Takashi Hachiya, Genki Nukazuka, Itaru Nakagawa

## Slide 2: Achievement by December, 2020
PC
Successfully Tracked down SC command transmission from PC to FPHX chip
Specified Chip-ID, Module SC
GUI Setting |  |  |  | SC Word |  |  |  |  | 
Module | Side | Chip | Gsel | Header* | Chip | Regist | instr | Data | Trailer
8 | 1 | 7 | 2 | 1100111 | 00111 | 01111 | 001 | 00000010 | 0000
15* | 15* | 21* | 2 | 1100111 | 10101 | 01111 | 001 | 00000010** | 0000
Observed SC word was exactly consistent with the command sent from Nevis GUI.
*Wildcard

## Slide 3: FPHX Readback Register Monitoring using the interception Board

## Slide 4: Observation of Register Readback
CH1: SC_OUT_0P
CH2: SC_OUT_0N
M: CH1-CH2
CH3: SC_IN_0P
CH4: SC_IN_0N
ROC->FPHX
Slow Control Command
FPHX->FPHX
Readback Register Word
Consistent pattern was observed.
GUI Setting |  |  |  | SC Word |  |  |  |  | 
Module | Side | Chip | Gsel | Header* | Chip | Regist | instr | Data | Trailer
8 | 1 | 5 | 2 | 1100111 | 00101 | 01111 | 001 | 01000010 | 0000
Data
Consistent pattern was observed.
Readback Register Word
(8bits)

## Slide 5: Observation of Register Readback
No readback when the wildcard is specified as described in the FPHX manual.

## Slide 6: SC Transmission to Specific CHIP-ID&Module
Tracing SC command transmission from PC to FPHX chip (done)
readback
Next step

## Slide 7: FEM Slow Control

## Slide 8: Slow Control Test Pin Map
GND | GND
7 | 15
6 | 14
5 | 13
4 | 12
3 | 11
2 | 10
1 | 9
0 | 8
GND | GND
SC_DATA_OUT[i] =DATA_TEST(i)
J3
Slow_Control_FEM.vhd
DATA FPGA Test pin Map
SlowControl FPGA Test pin Map

## Slide 9: FEM Slow Control FPGA I/O Structure
Readback From ROC thru SC fiber
14 bits SC_DATA_IN
(This is the data from the SC fiber)
Readback Register Word 8bits at FPHX out is converted into 14bits data word in ROC by the time received at FEM SC FPGA.
D0_SC_VME in SlowControl_FEM.vhd

## Slide 10: SlowControl_FEM.vhd
SC_DATA_IN is passed into DATA_RX_BUF
SlowControl_FEM.vhd: signal DATA_RX_BUF : std_logic_vector (13 downto 0);
DATA_RX_BUFの使用箇所リストは次頁

## Slide 11: DATA_RX_BUF(14bits);
MacBook-Pro-7:1008SlowControl_FEM_2Apr13 itaru$ grep DATA_RX_BUF *.vhd
SlowControl_FEM.vhd: signal DATA_RX_BUF : std_logic_vector (13 downto 0);
SlowControl_FEM.vhd: BUSY_ROC_SC <= DATA_RX_BUF(1) when (SYNC_OK = '1') else '0';
SlowControl_FEM.vhd: BUSY_CALIB <= DATA_RX_BUF(0) when (SYNC_OK = '1') else '0';
SlowControl_FEM.vhd: CLK_START_SC <= DATA_RX_BUF(11);
SlowControl_FEM.vhd: CS_FROM_ROC <= DATA_RX_BUF(10); CS=Chip Select
SlowControl_FEM.vhd: DATA_FROM_ROC <= DATA_RX_BUF(9); ReadbackワードはこのDATA_RX_BUF(9)にシリアルで送られてくる。
SlowControl_FEM.vhd: DATA_RX_BUF <= (others => '0');
SlowControl_FEM.vhd: DATA_RX_BUF <= SC_DATA_IN;
SlowControl_FEM.vhd: DATA_IN => DATA_RX_BUF,
SlowControl_FEM.vhd: CALIB_TRIGGER <= DATA_RX_BUF(2) and SYNC_OK;
SlowControl_FEM.vhd: AMPL_OUT(5 downto 0) <= DATA_RX_BUF(8 downto 3) when (SYNC_OK = ‘1’) else (others => ‘0’); キャリブレーションパルスのAmplitudeが8から3ビット目（5bit)に格納されてROCから送られてくるらしい。このAmplitudeはFEMでデータストリームに書き加えられるのか？
キャリブレーションデータ収集の最中は、ROCからAmplitudeやcalibration triggerシグナルが格納される。

## Slide 12: Module roc_serial_output
Inst_roc_serial_output: roc_serial_output PORT MAP(
RST => RST,
BCO_CLK => BCO_CLK,
SCK_EEPROM => SCK_EEPROM_int,
CS_IN => CS_FROM_ROC,
DATA_IN => DATA_FROM_ROC, 入力
SYNC_OK => SYNC_OK,
CS_OUT => ROC_CS,
DATA_OUT => ROC_DATA 出力
}
ROC_DATA => DATA_TO_SERIAL_OUTへ（次頁）

## Slide 13: ROC_DATA Test-pin Output Check
CH1: ROC_DATA
CH2: SC_OUT_0P
CH3: SC_OUT_0N
M: CH１-CH２
CH4: SC_IN_0P
OK, consistent test-pin out data is confirmed with register readback pattern (M:CH1-CH2)

## Slide 14: ROC_DATA Consistency Check
FPHXからのReadbackは正しいパターンだが、
ROC_DATAが正しいパターンが観測されない例

## Slide 15: SlowControl_FEM.vhd
DATA_TO_SERIAL_OUTPUT <= ROC_DATA
DATA_TO_SERIAL_OUTPUT => DATA_OUT_SC_int
DATA_OUT_SC_int => D0_SC_VME
これでVMEバックプレーンに流され、FEM-IBに送られる。
ここでデータビットが増えている(13ビット以上)
ROC_DATA=>DATA_TO_SERIAL_OUTPUT
=>DATA_OUT_SC_intのデータは整合性が取れていることは確認が取れた。

## Slide 16: DATA_OUT_SC_int
LVDS=171mA (10101011)
LVDS=3mA (00000011)
Doesn’t seem to be consistent.

## Slide 17: DATA_OUT_SC_int
LVDS=171mA (10101011)
LVDS=3mA (00000011)
11010101
1110000??

## Slide 18: Monitoring Register Readback at FEM-SC

## Slide 19: 2021年4月のReadbackerデバッグまとめ
InterceptionボードでモニターしたFPHXチップからのRegister Readbackは8bitの正しいパターンが帰ってきている。
Readbackの8bitワードはROCを経由してFEMのSlowControl_FEMに届いている。
ROC_DATAに格納されたデータワードは、FPHXチップが返したRegisterパターンと同じ時と、違う場合がある。典型的にはビット落ちのような症状で、立つべきBitが立っていない。
SlowControl_FEM.vhdの中でROC_DATA => DATA_TO_SERIAL_OUTPUT=>DATA_OUT_SC_int とbitサイズが変わっても、データは常に同じであることは確認できた。

## Slide 20: SC Transmission to Specific CHIP-ID&Module
Tracing SC command transmission from PC to FPHX chip (done)
readback
△
現時点では不十分

## Slide 21: 課題
今回使ったテストベンチ版のSlowControl_FEM.vhdでは、1008版と違い、ROCが帰すデータ書式とFEM側で受け取る書式が非互換かもしれない。1008版とテストベンチ版の比較をする。
ROC_DATAよりも上流、SC_DATA_INやDATA_RX_BUFをテストピンに出力して確認する。
FEMのSlow Controlで正しく受け取れ、VMEに正しく出力ができていることが確認できたら、FEM-IBの受信のチェックに進む。

## Slide 22: FEM-IB

## Slide 23: FEM-IB I/O Structure
DI_SC_VMEか？

## Slide 24: FEM-IB_top.vhd (1008版)
DI_SC_VME
DI_SC_VMEを出力してみる。

## Slide 25: ETH vs USB Output
1008版のFEM_IB_top.vhd
standalone版のFEM_IB_top.vhd
1008版とstandalone版のFEM_IB_top.vhdを比較すると、1008版のETHに出力するモジュールに相当するUSB出力モジュールがstandalone版には無いように見える。これはstandalone版に新たにUSBに出力するモジュールを追加しなければならなそう。
DATA_IO_USBを追加し、USE_USBでactivateするようなFunctionを追加

## Slide 26: ETH vs USB Output
この辺りのETH出力関係がTB版にはない。