## Slide 1: Commissioning of a hadron blind detector for dielectron measurement in pA reactions at J-PARC
Koki KANNO for the J-PARC E16 Collaboration
RIKEN

## Slide 2: Outline
J-PARC E16 experiment
hadron blind detector (HBD)
HBD commissioning
results
conclusions and outlook

## Slide 3: J-PARC E16 experiment
dielectron() measurement
  30 GeV p+A (fixed target), 10 MHz interaction
  eID for up to ~3 GeV/c electrons
6 mod. installed for the commissioning run
  26 mod. for the final design
beam
beam
Tracking detectors
Hadron blind detector
Lead-glass calorimeter

## Slide 4: Hadron blind detector (overview)
windowless and mirrorless proximity focus Cherenkov detector
  originally developed by the PHENIX experiment
  utilized for eID
  Triple GEM stack + CsI photocathode
  ionized electrons swept into mesh
  pad readout+APV25 hybrid card of SRS
  ASD connected to the bottom GEM for a trigger signal
Triple GEM
CsI photocathode
Incident electron
CF4 radiator
mesh
Readout pad

## Slide 5: Hadron blind detector (GEM)
30x30 cm2 GEM foils are used for the HBD
  made by Japanese company
  3 foils per stack, 4 stacks per module
  6 modules = 72 foils installed for the commissioning
CsI is evaporated on the top surface of the top GEM
  evaporated by Hamamatsu
Triple GEM
CsI photocathode
Incident electron
CF4 radiator
mesh
Readout pad
CsI evaporated GEM

## Slide 6: Hadron blind detector (front-end)
two types of readouts are used for the HBD
  pad readout with APV25 hybrid cards of SRS (1400 ch/module)
  the bottom surface of the bottom GEM with ASD for the trigger signal (36 ch/module)
Triple GEM
CsI photocathode
Incident electron
CF4 radiator
mesh
Readout pad
pad readout board
APV25 hybrid card
trigger ASD

## Slide 7
30 GeV proton beam
Lead-glass calorimeter
HBD
GEM tracker+SSD
Spectrometer commissioning

## Slide 8: Analysis (waveform)
signals are samples with 41.67 MHz (24 ns/cycle)
  with APV25 hybrid card of SRS
fitting w/ a function based on apv25 circuit constants
  a waveform template obtained with a test pulse does not reproduce well
time [ns]
ADC
chi2/ndf
events

## Slide 9: Analysis (clustering)
the side length of a hexagonal pad is 10 mm and it is smaller than the circular image of the Cherenkov photons
  circular image is φ34 mm when incident angle is 0 degree under the zero magnetic field
the neighboring fired pads are defined to belong to the same cluster
  a fired pad is defined to have a greater signal than 4σ of electric noise
10 mm
cluster charge:
sum of charge of fired pads in a given cluster
cluster size:
the number of fired pads in a given cluster

## Slide 10: Gain calibration
gas gain of a triple GEM stack is measured with scintillation photons induced by incident charged tracks
  radiator and working gas of CF4 is a good scintillator
exponential curve at low amplitudes attributed to scintillation photons
  gas gain distribution follows the Polya distribution
ave. gain fluctuation < 10%
pos. dependent gain fluctuation σ~30%
ADC
events
time
rel. gain

## Slide 11: Gas system
a recirculating gas system is implemented to reduce gas consumption and running costs
photon wavelength of interest ranges VUV region (100—200 nm)
kept H2O and O2 reasonably low over 2 weeks
  less than 5% loss of photoelectron
fresh gas
~0.4 L/min
HBD1
280 L
HBD2
280 L
HBD3
280 L
H2O/O2
analyzer
H2O/O2
analyzer
H2O/O2
analyzer
purifier
vent
~0.4 L/min
H2O
O2
ppm
time
2 weeks
purified gas
~7 L/min

## Slide 12: HBD response to pion
search for a HBD signal around the projected position of a track
  tracking with SSD and GEM trackers in front of the HBD
  pion ID with lead-glass calorimeter behind the HBD
ave. charge and cluster size are both consistent with the expected result
hit threshold
photoelectron
counts
cluster size
counts

## Slide 13: HBD response to electron
Lead-glass calorimeter is used for eID and position matching
we observed 11±1 p.e.
expected performance is 11＋1 p.e. and consistent with the observed result
an electron candidate leaves a multiple-pads hit
Poisson mean
λ: 11±1 p.e.
photoelectron
photoelectron
counts
counts
counts
cluster size
pion w/ LG
electron w/ LG

## Slide 14: Trigger efficiency
HBD issues a trigger signal via ASD connected to the bottom surface of the bottom GEM
  30x30 cm2 GEM foil segmented into 9 trigger-tiles
due to noise, a very shallow curve around the threshold is observed
  detector capacitance of each segment is ~5 nF
ASD threshold
photoelectron
9 ch
trig. eff.

## Slide 15: Electron detection efficiency and pion rejection power
electron detection efficiency and pion rejection power at both the trigger level and the offline level are evaluated
  At the trigger level, only a charge threshold is applied in an ASD board
  At the offline level, a threshold for charge cluster size is applied as well as trigger level condition
pion rejection power at the trigger level is worse than we had expected due to noise of ASD
  noise control
  DAQ upgrade
 | eID efficiency observed/expected | pion rejection power observed/expected
trigger level | 0.63±0.03/0.68 | 0.043±0.005/0.02
offline level | 0.61±0.04/0.63 | 0.009±0.002/0.006

## Slide 16: Conclusions and outlook
we performed commissioning runs for the J-PARC E16 spectrometer which was design to measure dielectron spectrum
Hadron blind detector is utilized for eID and works
  expected response to electrons and pions
  recirculating gas system
ASD board for a trigger signal is so noisy that pion contamination increases
noise control by grounding and DAQ upgrade are on-going for the next beam time